MOPAC 6.00 RELEASE NOTES
   
   
   
   
   
                       Notes summarizing the changes in MOPAC
                      in going from MOPAC 5.00 to MOPAC 6.00.
   
   
   
   
   
   
                                         by
   
   
   
   
   
   
                                James J. P. Stewart,
   
                        Frank J. Seiler Research Laboratory
                          United States Air Force Academy
                                      CO 80840
   
   
   
   
   
   
   
   
   
   
                                    October 1990
   
   
   
                                         
   
   

   
   
   
   
   
   
                                      CONTENTS
   
   
   
   CHAPTER 1       INTRODUCTION
   
           1.1     REDEFINED KEYWORDS . . . . . . . . . . . . . . . . 1-1
           1.2     GENERAL  . . . . . . . . . . . . . . . . . . . . . 1-2
           1.3     CORRECTION OF FAULTS IN MOPAC 5.0  . . . . . . . . 1-3
           1.4     INCREASES IN EFFICIENCY  . . . . . . . . . . . . . 1-4
           1.5     CRITERIA, LAYOUT, AND HOUSEKEEPING CHANGES . . . . 1-5
           1.6     IMPROVED OR NEW FUNCTIONALITIES  . . . . . . . . . 1-9
           1.7     EXTENSION TO NEW ELEMENTS. . . . . . . . . . . .  1-10
   
   
   CHAPTER 2       DEFINITIONS FOR NEW KEYWORDS
   
           2.1     NEW KEY WORDS  . . . . . . . . . . . . . . . . . . 2-1
           2.2     KEYWORDS THAT GO TOGETHER  . . . . . . . . . . .  2-10
   
   
   CHAPTER 3       BACKGROUND
   
           3.1     AIDER  . . . . . . . . . . . . . . . . . . . . . . 3-1
           3.2     GAUSSIAN Z-MATRICES  . . . . . . . . . . . . . . . 3-2
   
   
   CHAPTER 4       REFERENCES
   
   

   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
                                     CHAPTER 1
   
                                    INTRODUCTION
   
   
   
                             Introduction to MOPAC 6.0
                            for Experienced MOPAC Users
   
   
                                   Why Read This?
   
           Readers are assumed to  be  familiar  with  MOPAC  data  input  and
      output.  While the MOPAC 6.0 Manual contains a full description of these
      functions, experienced users can more easily learn about  MOPAC  6.0  by
      reference to the changes relative to MOPAC 5.0.  This document should be
      read once, then discarded.  Thereafter, reference to MOPAC 6.0 should be
      through the Manual or through the on-line HELP utility.
   
           Note that the Manual will  have  slightly  different  wording  from
      these upgrade notes:  the Manual is intended to be a reference document.
      These notes are intended to be read once only.
   
           Of paramount importance is the redefinition of the  keywords  DEBUG
      and 1SCF.
   
   
   
   
      1.1  REDEFINED KEYWORDS
   
           DEBUG:  Previously, DEBUG meant 'increase the amount of output when
      other keywords were used.' With the passage of time, more and more debug
      keywords have been defined.  Rather than define  all  allowed  keywords,
      existing debug keywords, such as FLEPO, LINMIN, etc.  have been removed,
      and are assumed to be debug keywords  if  'DEBUG'  is  specified.   Now,
      'DEBUG'  means  'all  unrecognized  keywords  are  assumed  to  be debug
      keywords'.  A few keywords,  such  as  VECTORS  and  DENSITY,  are  both
      recognized  and  debug  keywords:   recognized  to be both as legitimate
      keywords (VECTORS will cause the final eigenvectors to be printed),  and
      as  debug keywords, in that they cause increased diagnostic output to be
      generated when DEBUG is also used (VECTORS will cause  all  eigenvectors
   
                                        1-1
   

   
   
                                    INTRODUCTION
   
   
      on every iteration to be printed).
   
           1SCF:  Previously,  1SCF  would  not  generate  derivatives  unless
      GRADIENTS  was  also  specified,  in  which  case  all  derivatives were
      generated.  This choice of function had been made because half  electron
      derivatives took so long.
   
           With the analytic C.I.  derivatives, the time constraint is lifted.
      In  order  to  accommodate the new Gaussian options a new definition for
      1SCF became desirable.
   
           1SCF Definition:  A single SCF calculation will be done.   If  GRAD
      is also specified, gradients for the marked parameters will be generated
      and printed.  Under no circumstances will optimization or symmetry  data
      be changed.
   
   
   
   
   
      1.2  GENERAL
   
           The new keyword SETUP is recommended for general  use.   The  SETUP
      file  should  contain all commonly-used keywords.  If the default values
      of criteria are  not  acceptable,  then  the  desired  criteria  can  be
      specified  in  SETUP.   Each  data-set  could  then use SETUP.  If, in a
      specific job, the defaults in SETUP need to be changed, then specify the
      the  new  value  on  the  keyword  line.  The order of priority is thus:
      keywords take priority over SETUP, which takes  priority  over  built-in
      default values.
   
   
                    CHANGES IN GOING FROM MOPAC 5.0 TO MOPAC 6.0
   
           The changes made to MOPAC 5.0 in order to create MOPAC 6.0  can  be
      divided  into  the  following groups:  (a) correction of faults in MOPAC
      5.0; (b) changes to increase the speed of execution; (c) minor  criteria
      and layout changes; (d) improved or new algorithms; (e) extension to new
      elements.
   
           The main change that users should be aware of  is  that  much  more
      control  over  the calculation has been made available to the user.  The
      keyword PRECISE is retained, but is not  recommended.   PRECISE  is  too
      heavy-handed.   Most  of  the time it is sufficient to tighten up one or
      two criteria, rather that tighten up everything.  In particular, PRECISE
      should not routinely be used in conjunction with FORCE.
   
           Other examples of increased user control:
   
   
   
   
                                        1-2
   

   
   
                                    INTRODUCTION
   
   
           (a) In Version 5.0, if C.I.=4 was specified,  exactly  4  electrons
      were  involved  in  the  C.I.   In  Version 6.0, the user can select the
      number of electrons involved in the C.I.
   
           (b) In Version 5.0, users could not suppress  certain  output,  for
      example  the  DRC  geometries.   This frequently resulted in huge output
      files.  Version 6.0 gives  the  user  extensive  control  over  what  is
      printed in DRC's and IRC's.
   
           (c)  Additional  diagnostics  are  provided   to   allow   detailed
      monitoring of a calculation.
   
   
   
   
      1.3  CORRECTION OF FAULTS IN MOPAC 5.0
   
   
           1.  Force   constants   and   frequencies   calculated   using    a
               non-variationally optimized wavefunction were frequently faulty
               due to array overwrites.  This has  been  completely  reworked,
               and is now corrected.
   
           2.  When a text line was 'full', i.e.  no  double  spaces  and  the
               first  character  was not a space, MOPAC 5.00 would corrupt the
               last word.  This has  been  corrected  in  lines  2  and  3  by
               extending  the  strings  to  81  characters.   Line  1 has been
               completely re-defined (see later).
   
           3.  The torsion angle calculation was very  clumsy,  and  sometimes
               produced incorrect results.  This has been completely rewritten
               by Dr George Purvis III, of Tektronix, and is now 'bugfree'.
   
           4.  When PRECISE was used in a FORCE calculation  on  diatomic  and
               triatomic  systems,  the  trivial  modes had large frequencies.
               Constraints have now been placed  on  the  step  size  used  in
               calculating  the  Hessian.   Other  modes  were  not  affected.
               PRECISE is NOT recommended for use with FORCE calculations.
   
           5.  In FORCE  calculations  involving  large  numbers  of  hydrogen
               atoms,  the diagonalization would sometimes not work.  This bug
               was reported by Dr Yoshihisa Inoue of the Green Cross Corp.  of
               Osaka, Japan, along with a suggested fix.  The diagonalizer has
               been corrected, and such calculations should now work.
   
           6.  The EXTERNAL option would only work with AM1.  In Version  6.0,
               EXTERNAL will work with MNDO, AM1 and PM3.
   
           7.  In going from MOPAC  4.0  to  MOPAC  5.0,  an  error  had  been
               introduced   into  the  vibrational  transition  dipoles.   The
               magnitudes were wrong by about 30%.  This has been corrected in
   
                                        1-3
   

   
   
                                    INTRODUCTION
   
   
               Version 6.0.
   
           8.  In Version 5.0, if two atoms were  coincident,  then  a  divide
               error  would  occur.  This resulted in a job crash.  In Version
               6.0, those conditions  would  cause  an  error  message  to  be
               printed, and the run stopped.
   
   
   
   
   
   
      1.4  INCREASES IN EFFICIENCY
   
   
           1.  Where   possible,   the   finite-difference   derivatives    of
               non-variationally optimized wavefunctions (RHF open shell) have
               been replaced by the analytical derivatives described by  Dewar
               and  Liotard.   These are extremely fast compared with full SCF
               derivatives, and are normally highly accurate.  The derivatives
               can be used for all four Hamiltonians.
   
                    Limitations:  For reasons still unknown, if the  state  to
               be  optimized is very different from the ground state, then the
               computed  derivatives  have  unacceptably  large  errors.    To
               correct  this,  either  use  keyword  NOANCI or specify an open
               shell SCF wavefunction.   For  example,  to  optimize  the  9th
               excited state of formaldehyde, suitable keywords are "OPEN(2,3)
               C.I.=(3,0) ROOT=9" See also C.I.  (see later)
   
           2.  If, in a DRC, all forces on the atoms are  very  small  for  10
               consecutive steps (i.e.  the system has become quiescent), then
               the calculation will be stopped.
   
           3.  Prof Walter Thiel has proposed a new  strategy  for  optimizing
               geometries.   Some  of  his ideas have been incorporated into a
               new subroutine, FSTMIN, which replaces LINMIN.
   
           4.  Prof Peter Pulay's Geometric Direct Inversion of the  Iterative
               Subspace  technique  has been rendered into FORTRAN by Cummings
               and Gready.  Commings and Gready  volunteered  their  code  for
               incorporation  into  MOPAC.   The  G-DIIS  technique  does  not
               require  any  additional  function  evaluations,  and  is  thus
               'free'.  The implementation of the G-DIIS im MOPAC does not run
               as fast as that described by Cummings and Gready.  This is most
               likely  a  result  of  incorporating it into the existing MOPAC
               structure.
   
           5.  The two-electron two-center contributions to  the  Fock  matrix
               have been rewritten.
   
   
                                        1-4
   

   
   
                                    INTRODUCTION
   
   
           6.  The Eigenvector Following (EF) routine, as described by  Baker,
               has  been  added.   This  normally, but not always, runs faster
               than the BFGS.  For this reason, the EF is the  preferred  (but
               not the default) geometry optimization technique.  In addition,
               EF can locate and refine transition states  (new  keyword  TS).
               This  copy  of  EF is a slightly modified form of the procedure
               recommended by Baker, Jensen, Rzepa and Stebbings.
   
   
   
   
   
   
      1.5  CRITERIA, LAYOUT, AND HOUSEKEEPING CHANGES
   
   
           1.  The LOG file will now be created in the  directory  from  which
               the  job is run.  This seems more sensible than having it go to
               the root directory.  If you want the LOG file to go to the root
               directory, modify MOPAC.COM as indicated in MOPAC.COM.
   
           2.  Some information on the job will be  output  to  the  log  file
               unless  'NOLOG' is specified.  This will consist of the keyword
               lines, the "cycles", and a copy of the archive file:   This  is
               useful  for two reasons:  (a) monitoring a running job, and (b)
               In case of a machine crash, which sometimes causes the OUT  and
               ARC files to be lost, the LOG file will normally survive.
   
           3.  The whole data-set is read in at the very start of a  run,  and
               put  into  a  scratch  file.   This  frees up the data-set in a
               transparent manner.
   
           4.  A normal MOPAC Z-matrix will no longer need  the  extra  zero's
               for  atoms  2  or  3,  even  if the connectivity is explicitely
               given.  Thus, the geometry of formaldehyde could be written as:
   
                  C                                        C
                  O  1.2 1                    instead of   O  1.2 1
                  H  1.1 1 120 1       1 2                 H  1.1 1 120 1   0 0 1 2
                  H  1.1 1 120 1 180 0 1 2 3               H  1.1 1 120 1 180 0 1 2 3
   
   
           5.  Element Specification:  In addition  to  the  chemical  symbol,
               users  can now add a brief (6 character) description of an atom
               by enclosing the description within brackets, e.g.  Br(Bridge),
               C(Me),  P(V),  H(on C23).  Some care should be exercised if the
               output is to be read in to another program, as the layout  will
               begin  to  change  when  any  discription  involves more than 3
               characters.
   
   
   
                                        1-5
   

   
   
                                    INTRODUCTION
   
   
                    Dummy atoms can now be specified by the symbol 'X' or 'x',
               in  addition  to the current symbols 'XX', 'Xx', etc, and '99'.
               This change has been made to accommodate GAUSSIAN Z-matrices.
   
           6.  Version 6.0 will now allow multiple data-sets to be run as part
               of  one job.  The program is designed to consider each data-set
               as a wholly new calculation.  Thus, the first calculation might
               be  an  AM1  FORCE  calculation,  and the second a PM3 geometry
               optimization.  Limitations:  Except for the  first  system,  no
               system  must  cause  the  data-set  to be rewound.  Examples of
               data-sets which would cause a rewind are:
   
               1.  C.I.  calculations where the keyword MICROS is used.
   
               2.  Gaussian Z-matrices when the keyword AIGIN is NOT used.
   
               3.  When ab-initio gradients are read in, using keyword AIDER.
   
               4.  If ECHO is used.
   
   
           7.  In addition to internal and cartesian coordinates,  MOPAC  will
               now  allow  GAUSSIAN geometry files to be read in.  Most of the
               time, the file will be recognized automatically, but  for  very
               small  files  (two atom systems), the user will need to specify
               AIGIN.  If GAUSSIAN input is used, only one molecule can be run
               at  a  time,  unless  AIGIN  is  specified.   (MOPAC now allows
               several molecules to be run one after the other)
   
           8.  Energy gradients can be read in.  These  can  be  used  in  the
               calculation of ab initio stationary points.  See "Background".
   
           9.  The SCF criterion has been re-defined.  The new  SCF  criterion
               is  defined  as  follows:  "An SCF is assumed to exist when the
               energy change, in kcal/mol, drops below  SCFCRT  on  successive
               iterations".   There  are  other minor qualifications regarding
               the density matrix, but an SCF is defined mainly  in  terms  of
               energy fluctuation.  The other qualifications impose additional
               criteria on the SCF, and do not relax it.
   
          10.  Up to three lines are now  allowed  for  keywords.   Three  new
               keywords are used to define the keyword lines.  These are:
   
               1.  +:  A ' +' sign means  'read  another  line  of  keywords'.
                   Note  the  space  before  the  '+'  sign.   Since  '+' is a
                   keyword, it must be preceeded by a space.  A ' +' on line 1
                   would  mean  that  a second line of keywords should be read
                   in.  If that second line containes a  ' +',  then  a  third
                   line  of keywords will be read in.  Regardless of whether a
                   second or a third line of keywords is read in, the next two
                   lines will be description lines.
   
                                        1-6
   

   
   
                                    INTRODUCTION
   
   
                        Example of ' +' option
                       RESTART T=4D FORCE OPEN(2,2) SHIFT=20 PM3 +
                       SCFCRT=1.D-8 DEBUG ISOTOPE FMAT ECHO +
                       THERMO(300,400,1) ROT=3
                       [Example of data set with three lines of keywords.]
                       NOTE: There are two lines of description.]
   
               2.  &:  An ' &' means 'turn the next line  into  keywords'.   A
                   ' &'  on  line  1 would mean that a second line of keywords
                   should be read in.  If that second line containes  a  ' &',
                   then  a  third  line  of  keywords will be read in.  If the
                   first line has a ' &' then the first  description  line  is
                   omitted,   if  the  second  line  has  a  ' &',  then  both
                   description lines are omitted.
   
               3.  SETUP:  If, on  the  keyword  line,  the  word  'SETUP'  is
                   specified,  then  one or two lines of keywords will be read
                   from a file with the logical name SETUP.   The  file  SETUP
                   must  exist,  and  must  contain at least one line.  If the
                   second line of the data-set is defined by the first line as
                                                        _
                   a  keyword  line  (by  a  +  or  an  ), and the second line
                   contains the word SETUP, then one line of keywords will  be
                   read from a file with the logical name SETUP.  SETUP can be
                   followed, optionally, by the logical name, or the  name  of
                   the   file,   which   holds   the   SETUP  keywords,  e.g.,
                   SETUP=mydata.keys, SETUP=fred,  in  which  case  the  SETUP
                   keywords  are in the file mydata.keys, or the file with the
                   logical name fred.
   
   
                    The following table illustrates the allowed combinations
          Line 1      Line 2     Line 3  Line 4   Line 5  Setup used
   
          Keys        Text       Text   Z-matrix Z-matrix  not used 
          Keys +      Keys       Text    Text    Z-matrix  not used
          Keys +      Keys +     Keys    Text    Text      not used
          Keys &      Keys       Text   Z-matrix Z-matrix  not used
          Keys &      Keys &     Keys   Z-matrix Z-matrix  not used
          Keys SETUP  Text       Text   Z-matrix Z-matrix 1 or 2 lines used
          Keys +      Keys SETUP Text    Text    Z-matrix 1 line used
          Keys &      Keys SETUP Text   Z-matrix Z-matrix 1 line used
   
                No other combinations are allowed.
   
                The proposed use of the SETUP option is to allow a  frequently
           used  set  of  keywords  to  be  defined  by a single keyword.  For
           example, if the default criteria  are  not  suitable,  SETUP  might
           contain
            " SCFCRT=1.D-8  SHIFT=30 ITRY=600 GNORM=0.02 ANALYT "
            "                                                   "
           The order of usage of a keyword is Line 1 > Line 2 > Line 3.   Line
   
                                        1-7
   

   
   
                                    INTRODUCTION
   
   
           1 > SETUP.  Line 2 > SETUP.  SETUP > built in default values.
   
      11.  Because of the steadily increasing number of keywords, a change has
           been  made  which  will allow a large number of keywords to be used
           without having a very large WRTKEY subroutine.  (WRTKEY checks  the
           validity  of  keywords,  and  prints  all  keywords used.) Now, all
           keywords which print details of subroutines will not be  explicitly
           recognized.    Instead,   if  DEBUG  is  specified,  all  otherwise
           unrecognized keywords will be assumed to be  valid  keywords.   The
           main  effect  is  that keywords such as FLEPO, LINMIN, MOLDAT, etc.
           are now not valid keywords, but can be used if the keyword DEBUG is
           also specified.
   
      12.  To save space, DRC and IRC outputs will, by default, only print the
           line with the percent sign.  Other output can be obtained by use of
           the keyword LARGE, according to the following rules:
   
              Keyword             Effect
              LARGE          Print all internal and cartesian coordinates 
                             and cartesian velocities.
              LARGE=1        Print all internal coordinates.
              LARGE=-1       Print all internal and cartesian coordinates 
                             and cartesian velocities.
              LARGE=n        Print every n'th set of internal coordinates.
              LARGE=-n       Print every n'th set of internal and cartesian 
                             coordinates and cartesian velocities.
   
                If LARGE=1 is used, the output will be the  same  as  that  of
           Version 5.0, when LARGE was not used.  If LARGE is used, the output
           will be the same as that of Version 5.0, when LARGE was  used.   To
           save disk space, do not use LARGE.
   
      13.  In order to allow  MOPAC  to  be  run  on  machines  which  do  not
           automatically  SAVE variables, many (but not all) variables are now
           SAVED.
   
      14.  A second copy of the ARCHIVE file is now automatically  written  to
           the LOG file.  This can be suppressed by specifying "NOLOG".
   
   
   
   
   
   
   
   
   
   
   
   
   
   
                                        1-8
   

   
   
                                    INTRODUCTION
   
   
      1.6  IMPROVED OR NEW FUNCTIONALITIES
   
   
           1.  A completely new  functionality,  the  ElectroStatic  Potential
               calculation  of  Besler,  Merz,  and  Kollman,  has been added.
               Because of its size, it is not part of the default  MOPAC,  but
               can  be  added  at  any  time.  Instructions on this are in the
               Manual.
   
           2.  The C.I.  keyword has been extended  to  allow  the  number  of
               doubly-filled  levels  to be specified.  The extended format is
               C.I.=(N,M), where N is the number  of  M.O.s  involved  in  the
               C.I., and M is the number of filled levels.
   
   
                                          EXAMPLES
                  Keywords           Number of M.O.s  No. Electrons
   
                  C.I.=2                   2             2 (1)
                  C.I.=(2,1)               2             2 (3)
                  C.I.=(3,1)               3             2 (3)
                  C.I.=(3,2)               3             4 (5)
                  C.I.=(3,0) OPEN(2,3)     3             2 (N/A)
                  C.I.=(3,1) OPEN(2,2)     3             4 (N/A)
                  C.I.=(3,1) OPEN(1,2)     3           N/A (3)
   
                Odd electron systems given in parentheses.
   
           3.  Phonon  and  electronic  band  structure   calculation.    Both
               calculations can be run on a polymer.  The same keyword is used
               to specify both.  Which calculation is actually run depends  on
               other   keywords,   e.g.,  if  FORCE  is  specified,  a  phonon
               calculation will be run, otherwise a band-structure calculation
               will be run.
   
           4.  The hyperpolarizability calculation has been made more precise.
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
                                        1-9
   

   
   
                                    INTRODUCTION
   
   
      1.7  EXTENSION TO NEW ELEMENTS.
   
   
           1.  AM1:  New elements added:  Aluminum, Phosphorus and Sulfur.
   
                    Editorial comment:
   
                    Extra  care  should  be  taken  when  using  aluminum   or
               phosphorus.  Both elements have sharp energy barriers, aluminum
               at 2.05 Angstroms and phosphorus at 3.0 Angstroms.   These  can
               severely  complicate  results.   Thus  Al2F6  has  three stable
               bridged configurations, and P4O6 and P4O10 are highly distorted
               relative   to  the  correct  Td  geometry,  the  P-P  distances
               differing by 0.4 Angstroms.
   
           2.  MNDO:  None.
   
           3.  PM3:  Beryllium, Magnesium, Zinc, Gallium, Germanium,  Arsenic,
               Selenium,  Cadmium,  Indium, Tin, Antimony, Tellurium, Mercury,
               Thallium, Lead, and Bismuth.
   
                    Editorial comment:
   
                    Extra  care  should  be  taken  with  cadmium  and   other
               elements.   The  paucity  of  reference data resulted in a high
               accuracy, poorly predictive method.
   
                    The full set of available PM3 elements is as follows:
                                       Elements available in PM3
   
                                     H
                                     **  Be      **  C   N   O   F
                                     **  Mg      Al  Si  P   S   Cl
                                     **  **  Zn  Ga  Ge  As  Se  Br
                                     **  **  Cd  In  Sn  Sb  Te  I
                                     **  **  Hg  Tl  Pb  Bi
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
                                        1-10
   

   
   
   
   
   
   
   
   
   
   
   
   
   
   
                                     CHAPTER 2
   
                            DEFINITIONS FOR NEW KEYWORDS
   
   
   
      2.1  NEW KEY WORDS
   
   
   
                                       & (C)
   
           An ' &' means 'turn the next line into keywords'.  A ' &' on line 1
      would  mean  that  a second line of keywords should be read in.  If that
      second line contained a ' &', then a third line  of  keywords  would  be
      read  in.   If the first line has a ' &' then the first description line
      is omitted, if the second line has a ' &', then both  description  lines
      are omitted.
   
           Examples
        Use of one '&'
   
       VECTORS DENSITY RESTART & NLLSQ T=1H SCFCRT=1.D-8 DUMP=30M ITRY=300 
       PM3 FOCK OPEN(2,2) ROOT=3 SINGLET SHIFT=30
       Test on a totally weird system
   
        Use of two '&'s
   
       LARGE=-10 & DRC=4.0 T=1H SCFCRT=1.D-8 DUMP=30M ITRY=300 SHIFT=30 
       PM3 OPEN(2,2) ROOT=3 SINGLET NOANCI ANALYT  T-PRIORITY=0.5 &
       LET GEO-OK VELOCITY KINETIC=5.0 
   
   
   
   
   
   
   
   
   
   
   
   
                                        2-1
   

   
   
                            DEFINITIONS FOR NEW KEYWORDS
   
   
                                       + (C)
   
           A ' +' sign means 'read another line of keywords'.  Note the  space
      before  the '+' sign.  Since '+' is a keyword, it must be preceeded by a
      space.  A ' +' on line 1 would mean  that  a  second  line  of  keywords
      should  be  read in.  If that second line containes a ' +', then a third
      line of keywords will be read in.  Regardless of whether a second  or  a
      third  line  of  keywords  is  read  in,  the  next  two  lines would be
      description lines.
   
           Example of ' +' option
   
          RESTART T=4D FORCE OPEN(2,2) SHIFT=20 PM3 +
          SCFCRT=1.D-8 DEBUG + ISOTOPE FMAT ECHO singlet ROOT=3
          THERMO(300,400,1) ROT=3
          [Example of data set with three lines of keywords.]
          NOTE: There are two lines of description.]
   
   
                                      1SCF (C)
   
           When users want to examine the results of a single SCF  calculation
      of  a  geometry,  1SCF  should be used.  1SCF can be used in conjunction
      with RESTART, in which case a single SCF calculation will be  done,  and
      the results printed.
   
           When 1SCF is used on its own (that is, RESTART is  not  also  used)
      then derivatives will only be calculated if GRAD is also specified.
   
           1SCF is helpful in a learning situation.  MOPAC  normally  performs
      many  SCF  calculations,  and in order to minimize output when following
      the working of the SCF calculation, 1SCF is very useful.
   
   
                                     AIDER (C)
   
           AIDER allows MOPAC to optimize an ab-initio geometry.  To  use  it,
      calculate  the  ab-initio gradients using, e.g., Gaussian.  Supply MOPAC
      with these gradients, after converting them into kcal/mol.  The geometry
      resulting  from  a  MOPAC  run will be nearer to the optimized ab-initio
      geometry than if the geometry optimizer in Gaussian had been used.
   
   
   
   
   
   
   
   
   
   
   
                                        2-2
   

   
   
                            DEFINITIONS FOR NEW KEYWORDS
   
   
                                     AIGIN (C)
   
           If the geometry (Z-matrix) is specified using the Gaussian-8X, then
      normally  this will be read in without difficulty.  In the event that it
      is mistaken for a normal  MOPAC-type  Z-matrix,  the  keyword  AIGIN  is
      provided.  As of the time of writing, no examples of data requiring this
      keyword have been made.  AIGIN  is  therefore  a  hedge  against  as-yet
      unknown  problems  with Z-matrices.  AIGIN will force the data-set to be
      read in assuming Gaussian format.  This is necessary if  more  than  one
      system is being studied in one run.
   
   
                                     AIGOUT (O)
   
           The ARCHIVE file contains a data-set  suitable  for  submission  to
      MOPAC.   If,  in  addition  to  this data-set, the Z-matrix for Gaussian
      input is wanted, then AIGOUT (ab  initio  geometry  output),  should  be
      used.
   
           The Z-matrix is in full Gaussian form.   Symmetry,  where  present,
      will be correctly defined.  Names of symbolics will be those used if the
      original geometry was in Gaussian format, otherwise 'logical' names will
      be used.  Logical names are of form <t><a><b>[<c>][<d>] where <t> is 'r'
      for bond length, 'a' for angle, or 'd' for dihedral,  <a>  is  the  atom
      number, <b> is the atom to which <a> is related, <c>, if present, is the
      atom number to which <a> makes an angle, and <d>,  if  present,  is  the
      atom number to which <a> makes a dihedral.
   
           If 1SCF is specified, extra care should be taken to ensure that the
      desired  format is generated.  If the 1SCF is used in conjunction with a
      RESTART, then the variables defined will be those of the  original  job.
      Otherwise,  by  default,  when  1SCF  is  specified,  gradients  are not
      calculated.  This means  that  all  variables  become  fixed,  i.e.,  no
      symbolics are used.  See also 1SCF and RESTART.
   
   
                                       DIPOLE
   
           Used in the ESP calculation, DIPOLE will constrain  the  calculated
      charges  to  reproduce the cartesian dipole moment components calculated
      from the density matrix and nuclear charges.
   
   
   
   
   
   
   
   
   
   
   
                                        2-3
   

   
   
                            DEFINITIONS FOR NEW KEYWORDS
   
   
                                        DIPX
      Similar to DIPOLE, except the fit will be for the X-component only.
   
   
                                        DIPY
      Similar to DIPOLE, except the fit will be for the Y-component only.
   
   
                                        DIPZ
      Similar to DIPOLE, except the fit will be for the Z-component only.
   
   
                                     DMAX=n.nn
   
           In the EF routine, the  maximum  step-size  is  0.2  (Angstroms  or
      radians),  by  default.   This  can  be changed by specifying DMAX=n.nn.
      Increasing DMAX can lead to faster convergence but  can  also  make  the
      optimization  go  bad  very fast.  Furthermore, the Hessian updating may
      deteriorate when using large stepsizes.  Reducing the stepsize  to  0.10
      or 0.05 is recommended when encountering convergence problems.
   
   
   
           EF (C)
   
           The Eigenvector Following routine is an alternative  to  the  BFGS,
      and  appears  to  be  much  faster.  To invoke the eigenvector following
      routine, specify EF.  EF is particularly good in the end-game, when  the
      gradient is small.  See also HESS, DMAX, EIGINV.
   
   
                                     EIGINV (W)
   
           Not recommended for normal use.  Used with  the  EF  routine.   See
      source code for more details.
   
   
                                        ESP
      This is  the  ElectroStatic  Potential  calculation  of  K. M. Merz  and
      B. H. Besler.    ESP   calculates   the   expectation   values   of  the
      electrostatic potential of a  molecule  on  a  uniform  distribution  of
      points.   The  resultant  ESP  surface  is  then fitted to atom centered
      charges that best reproduce the distribution, in a least squares sense.
   
   
   
   
   
   
   
   
   
                                        2-4
   

   
   
                            DEFINITIONS FOR NEW KEYWORDS
   
   
                                       ESPRST
      ESPRST restarts a stopped ESP calculation.  Do not use with RESTART.
   
   
                                     IUPD=n (W)
   
           IUPD is used only in the EF routine.  IUPD should  very  rarely  be
      touched.   IUPD=1  can  be  used  in minimum searches if the the message
      "HEREDITARY  POSITIVE  DEFINITENESS  ENDANGERED.   UPDATE  SKIPPED  THIS
      CYCLE"  occurs every cycle for 10-20 iterations.  Never use IUPD=2 for a
      TS search!  For more information, read the comments in subroutine EF.
   
   
                                     HESS=n (W)
   
           When  the  Eigenvector  Following  routine  is  used  for  geometry
      optimization,  it  frequently works faster if the Hessian is constructed
      first.  If HESS=1 is specified, the Hessian matrix will  be  constructed
      before  the  geometry  is  optimized.   There  are  other,  less common,
      options, e.g.  HESS=2.  See comments in subroutine EF for details.
   
   
                                   K=(n.nn,n) (C)
   
           Used  in  band-structure  calculations,  K=(n.nn,n)  specifies  the
      step-size  in  the  Brillouin  zone,  and  the  number  of  atoms in the
      monomeric  unit.   Two  band-structure   calculations   are   supported:
      electronic  and phonon.  Both require a polymer to be used.  If FORCE is
      used, a  phonon  spectrum  is  assumed,  otherwise  an  electronic  band
      structure  is  assumed.   For  both calculations, a density of states is
      also done.  The band structure calculation is  very  fast,  so  a  small
      step-size will not use much time.
   
           The output is designed to be fed into a graphics  package,  and  is
      not   'elegant'.    For   polyethylene,  a  suitable  keyword  would  be
      K=(0.01,6).
   
   
                                      MODE (C)
   
           MODE is used in the EF routine.  Normally  the  default  MODE=1  is
      used  to locate a transition state, but if this is incorrect, explicitly
      define the vector to be followed by MODE=n.  (MODE is not a  recommended
      keyword).   If  you  use  the  FORCE  option when deciding which mode to
      follow, set all isotopic masses to 1.0.  The normal modes from FORCE are
      normally mass-weighted; this can mislead.  Alternatively, use LARGE with
      FORCE:  this gives the force constants and vectors in  addition  to  the
      mass-weighted  normal  modes.  Only the mass-weighted modes can be drawn
      with DRAW.
   
   
   
                                        2-5
   

   
   
                            DEFINITIONS FOR NEW KEYWORDS
   
   
                                        MS=n
   
           Useful for checking the MECI calculation and  for  teaching.   MS=n
      overrides the normal choice of magnetic component of spin.  Normally, if
      a triplet is requested, a MS of  1  will  be  used;  this  excludes  all
      singlets.  If MS=0 is also given, then singlets will also be calculated.
      The use of MS should not affect the values of the results at all.
   
   
                                     NOANCI (W)
   
           RHF open-shell derivatives are normally calculated using  Liotard's
      analytical  C.I.   method.   If  this  method is NOT to ne used, specify
      NOANCI (NO ANalytical Configuration Interaction derivatives).
   
   
                                     NODIIS (W)
   
           In the event that the G-DIIS option is not wanted,  NODIIS  can  be
      used.   The  G-DIIS  normally accelerates the geometry optimization, but
      there is no guarantee that it will do so.   If  the  heat  of  formation
      rises unexpectedly (i.e.  rises during a geometry optimization while the
      GNORM is larger than about 0.3), then try NODIIS.
   
   
                                     NOLOG (O)
   
           Normally a copy of the archive file will be  directed  to  the  LOG
      file,  along  with a synopsis of the job.  If this is not wanted, it can
      be suppressed completely by NOLOG.
   
   
                                      NONR (W)
   
           Not recommended for normal use.  Used with  the  EF  routine.   See
      source code for more details.
   
   
                                    NOTHIEL (W)
   
           In a normal geometry optimization using the BFGS  routine,  Thiel's
      FSTMIN  technique  is used.  If normal line-searches are wanted, specify
      NOTHIEL.
   
   
   
   
   
   
   
   
   
                                        2-6
   

   
   
                            DEFINITIONS FOR NEW KEYWORDS
   
   
                                       NSURF
   
           In an ESP calculation, NSURF=n  specifies  the  number  of  surface
      layers for the Connolly surface.
   
   
                                     OLDGEO (C)
   
           If multiple geometries are to be run, and the final  geometry  from
      one  calculation  is  to  be  used to start the next calculation, OLDGEO
      should be specified.  Example:  If a MNDO, AM1, and PM3 calculation were
      to be done on one system, for which only a rough geometry was available,
      then after the MNDO calculation, the AM1 calculation could be done using
      the  optimized  MNDO  geometry  as  the starting geometry, by specifying
      OLDGEO.
   
   
                                     ORIDE (W)
   
           Do not use this keyword until you have read Simon's article.  ORIDE
      is  part  of the EF routine, and means "Use whatever Lamdas are produced
      even if they would normally be 'unacceptable'."
   
   
                                    POINT=n (C)
   
           The number of points  to  be  calculated  on  a  reaction  path  is
      specified by POINT=n.  Used only with STEP in a path calculation.
   
   
                                    POINT1=n (C)
   
           In a grid calculation, the number of points to be calculated in the
      first direction is given by POINT1=n.  'n' should be less than 24.
   
   
                                    POINT2=n (C)
   
           In a grid calculation, the number of points to be calculated in the
      second direction is given by POINT2=n.  'n' should be less than 24.
   
   
   
   
   
   
   
   
   
   
   
   
                                        2-7
   

   
   
                            DEFINITIONS FOR NEW KEYWORDS
   
   
                                       POTWRT
   
           In an ESP calculation, write out surface points  and  electrostatic
      potential values to UNIT 21.
   
   
                                      RECALC=n
   
           RECALC=n  calculates  the  Hessian  every  n  steps   in   the   EF
      optimization.   For small n this is costly but is also very effective in
      terms of  convergence.   RECALC=10  and  DMAX=0.10  can  be  useful  for
      difficult  cases.   In  extreme cases RECALC=1 and DMAX=0.05 will always
      find a stationary point, if it exists.
   
   
                                       SCALE
   
           SCALE=n.n specifies the scaling factor for Van der Waals' radii for
      the initial layer of the Connolly surface in the ESP calculation.
   
   
                                  SCFCRT=n.nn (W)
   
           The default SCF criterion is to be  replaced  by  that  defined  by
      SCFCRT=.
   
           The SCF criterion is the  change  in  energy  in  kcal/mol  on  two
      successive  iterations.   Other minor criteria may make the requirements
      for an SCF slightly more stringent.  The SCF  criterion  can  be  varied
      from  about  0.001  to  1.D-25,  although numbers in the range 0.0001 to
      1.D-9 will suffice for most applications.
   
   
                                    SCINCR=n.nn
   
           In an ESP calculation, SCINCR=n.nn specifies the increment  between
      layers of the surface in the Connolly surface.  (default:  0.20)
   
   
                                     SETUP (C)
   
           If, on the keyword line, the word 'SETUP' is specified, then one or
      two  lines  of  keywords  will be read from a file with the logical name
      SETUP.  The logical file SETUP must exist, and must contain at least one
      line.   If  the  second  line  is defined by the first line as a keyword
      line, and the second line contains the word  SETUP,  then  one  line  of
      keywords will be read from a file with the logical name SETUP.
   
   
   
   
   
                                        2-8
   

   
   
                            DEFINITIONS FOR NEW KEYWORDS
   
   
                                   SETUP=name (C)
   
           Same as SETUP, only the logical or actual name of the SETUP file is
      'name'.
   
   
                                       SLOPE
   
           In an ESP calculation, SLOPE=n.nn specifies the  scale  factor  for
      MNDO charges.  (default=1.422)
   
   
                                      STEP (C)
   
           In a reaction path, if the path step is constant, STEP can be  used
      instead  of  explicitly  specifying  each point.  The number of steps is
      given by POINT.  If the reaction coordinate is an interatomic  distance,
      only positive STEPs are allowed.
   
   
                                       SYMAVG
   
           Used by the ESP, SYMAVG will average charges which should have  the
      same value by symmetry.
   
   
                                       STO3G
   
           In an ESP calculation STO3G means "Use  the  STO-3G  basis  set  to
      de-orthogonalize the semiempirical orbitals".
   
   
                                       TS (C)
   
           Within the Eigenvector Following  routine,  the  option  exists  to
      optimize   a  transition  state.   To  do  this,  use  TS.   Preliminary
      indications are that the TS method is much faster and more reliable than
      either SIGMA or NLLSQ.
   
           TS appears to work well with cartesian coordinates.
   
   
   
   
   
   
   
   
   
   
   
   
                                        2-9
   

   
   
                            DEFINITIONS FOR NEW KEYWORDS
   
   
                                    WILLIAMS (C)
   
           Within the ESP calculation, the Connolly surface  is  used  as  the
      default.   If  the  surface  generation  procedure of Donald Williams is
      wanted, the keyword WILLIAMS should be used.
   
   
   
      2.2  KEYWORDS THAT GO TOGETHER
   
           Normally only a subset of keywords are used in any given  piece  of
      research.  Keywords which are related to each other in this way are:
   
           1.  In getting an SCF:  SHIFT, PULAY, ITRY, CAMP, SCFCRT, 1SCF, PL
   
           2.  In C.I.  work:  SINGLET, DOUBLET, etc., OPEN(n,m),  C.I.=(n,m),
               LARGE, MECI, MS=n, VECTORS, ESR, ROOT=n
   
           3.  In excited states:  UHF with  (TRIPLET,  QUARTET,  etc.),  C.I.
               keywords.
   
           4.  In geometry optimization:
   
               1.  Using BFGS:  GNORM=n.n, XYZ, PRECISE.
   
               2.  Using EF:  GNORM=n.n, XYZ, PRECISE
   
               3.  Using NLLSQ:  GNORM=n.n, XYZ, PRECISE
   
               4.  Using SIGMA:  GNORM=n.n, XYZ, PRECISE
   
   
           5.  In Gaussian work:  AIGIN, AIGOUT, AIDER.
   
           6.  In SADDLE:  XYZ, BAR=n.n
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
                                        2-10
   

   
   
   
   
   
   
   
   
   
   
   
   
   
   
                                     CHAPTER 3
   
                                     BACKGROUND
   
   
   
      3.1  AIDER
   
           AIDER will allow gradients to be defined for a system.  MOPAC  will
      calculate  gradients,  as  usual, and then use the supplied gradients to
      form an error function.  The error function  is  (supplied  gradients  -
      initial  calculated  gradients).   This  is  then  added to the computed
      gradients, so that for the initial  SCF,  the  apparent  gradients  will
      equal the supplied gradients.
   
           A typical data-set using AIDER would look like this:
         PM3 AIDER AIGOUT GNORM=0.01 EF
       Cyclohexane
   
        X  
        X     1    1.0
        C     1    CX    2  CXX
        C     1    CX    2  CXX    3  120.000000   
        C     1    CX    2  CXX    3 -120.000000   
        X     1    1.0   2  90.0   3    0.000000
        X     1    1.0   6  90.0   2  180.000000
        C     1    CX    7  CXX    3  180.000000   
        C     1    CX    7  CXX    3   60.000000   
        C     1    CX    7  CXX    3  -60.000000   
        H     3    H1C   1  H1CX   2    0.000000   
        H     4    H1C   1  H1CX   2    0.000000   
        H     5    H1C   1  H1CX   2    0.000000   
        H     8    H1C   1  H1CX   2  180.000000   
        H     9    H1C   1  H1CX   2  180.000000   
        H    10    H1C   1  H1CX   2  180.000000   
        H     3    H2C   1  H2CX   2  180.000000   
        H     4    H2C   1  H2CX   2  180.000000   
        H     5    H2C   1  H2CX   2  180.000000   
        H     8    H2C   1  H2CX   2    0.000000   
        H     9    H2C   1  H2CX   2    0.000000   
        H    10    H2C   1  H2CX   2    0.000000   
   
   
                                        3-1
   

   
   
                                     BACKGROUND
   
   
        CX      1.46613   
        H1C     1.10826   
        H2C     1.10684   
        CXX    80.83255 
        H1CX  103.17316
        H2CX  150.96100
   
        AIDER
          0.0000
         13.7589   -1.7383
         13.7589   -1.7383    0.0000
         13.7589   -1.7383    0.0000
          0.0000    0.0000    0.0000
          0.0000    0.0000    0.0000
         13.7589   -1.7383    0.0000
         13.7589   -1.7383    0.0000
         13.7589   -1.7383    0.0000
        -17.8599   -2.1083    0.0000
        -17.8599   -2.1083    0.0000
        -17.8599   -2.1083    0.0000
        -17.8599   -2.1083    0.0000
        -17.8599   -2.1083    0.0000
        -17.8599   -2.1083    0.0000
        -17.5612   -0.6001    0.0000
        -17.5612   -0.6001    0.0000
        -17.5612   -0.6001    0.0000
        -17.5612   -0.6001    0.0000
        -17.5612   -0.6001    0.0000
        -17.5612   -0.6001    0.0000
   
           Each  supplied  gradient  goes  with  the  corresponding   internal
      coordinate.   In  the  example  given,  the  gradients came from a 3-21G
      calculation on the geometry shown.  Symmetry will be taken into  account
      automatically.   Gaussian  prints  out  gradients in atomic units; these
      need to be converted into kcal/mol/Angstrom or kcal/mol/radian for MOPAC
      to use.  The resulting geometry from the MOPAC run will be nearer to the
      optimized 3-21G geometry than  if  the  normal  geometry  optimizers  in
      Gaussian had been used.
   
   
   
      3.2  GAUSSIAN Z-MATRICES
   
           With certain limitations, geometries can now  be  specified  within
      MOPAC using the Gaussian Z-matrix format.
   
   
   
   
   
   
   
                                        3-2
   

   
   
                                     BACKGROUND
   
   
                      Exceptions to the full Gaussian standard
   
           1.  The option of defining an atom's position by one  distance  and
               two  angles  is  not  allowed.  In other words, the N4 variable
               described in the Gaussian manual must either  be  zero  or  not
               specified.   MOPAC requires the geometry of atoms to be defined
               in terms  of,  at  most,  one  distance,  one  angle,  and  one
               dihedral.
   
           2.  Gaussian cartesian coordinates are not supported.
   
           3.  Chemical symbols must not be followed by an integer identifying
               the atom.  Numbers after a symbol are used by MOPAC to indicate
               isotopic mass.  If labels are desired, they should be  enclosed
               in parentheses, thus "Cl(on C5)34.96885"
   
           4.  The connectivity (N1, N2, N3) must be integers.  Labels are not
               allowed.
   
   
   
                       Specification of Gaussian Z-matrices.
   
           The information contained in the Gaussian Z-matrix is identical  to
      that in a MOPAC Z-matrix.  The order of presentation is different.  Atom
      N, (real or dummy) is specified in the format:
        Element   N1   Length  N2  Alpha   N3  Beta
   
           Where Element is the same as for the MOPAC Z-matrix.  N1,  N2,  and
      N3  are the connectivity, the same as the MOPAC Z-matrix NA, NB, and NC:
      bond lengths are between N and N1, angles are between N, N1 and N2,  and
      dihedrals  are  between  N, N1, N2, and N3.  The same rules apply to N1,
      N2, and N3 as to NA, NB, and NC.
   
           Length, Alpha and  Beta  are  the  bond  lengths,  the  angle,  and
      dihedral.   They can be real, e.g.  1.45, 109.4, 180.0, or 'logical'.  A
      logical is an alphanumeric string of up  to  8  characters,  e.g.   R51,
      A512,  D5213, CH, CHO, CHOC, etc.  Two or more logicals can be the same.
      Dihedral logicals can optionally be preceeded by a minus sign, in  which
      case  the  value  of  the  dihedral  is the negative of the value of the
      logical.  This is the equivalent of the normal MOPAC SYMMETRY operations
      1, 2, 3, and 14.
   
           If an internal coordinate is real, it will not be optimized.   This
      is  the  equivalent  of the MOPAC optimization flag "0".  If an internal
      coordinate is logical, it can be optimized.
   
           The Z-matrix is terminated by a blank line, after which  comes  the
      starting values of the logicals, one per line.  If there is a blank line
      in this set, then all logicals  after  the  blank  line  are  considered
      fixed;  that  is,  they will not be optimized.  The set before the blank
   
                                        3-3
   

   
   
                                     BACKGROUND
   
   
      line will be optimized.
   
           If a Gaussian Z-matrix is supplied, the keyword SYMMETRY should NOT
      be  specified,  even if symmetry is defined by the Z-matrix.  At the end
      of the job, if the MOPAC Z-matrix format is wanted, you will need to add
      SYMMETRY to the keyword line, if the Gaussian Z-matrix implied symmetry.
   
   
                Example of Gaussian Z-matrix geometry specification
   
         Line 1    AM1
         Line 2  Ethane                                   
         Line 3  
         Line 4    C  
         Line 5    C     1     r21    
         Line 6    H     2     r32       1     a321   
         Line 7    H     2     r32       1     a321      3  d4213
         Line 8    H     2     r32       1     a321      3 -d4213
         Line 9    H     1     r32       2     a321      3   60.
         Line 10   H     1     r32       2     a321      3  180.
         Line 11   H     1     r32       2     a321      3  d300
         Line 12 
         Line 13      r21        1.5
         Line 14      r32        1.1
         Line 15      a321     109.5
         Line 16      d4313    120.0
         Line 17
         Line 18      d300     300.0
         Line 19 
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
                                        3-4
   

   
   
   
   
   
   
   
   
   
   
   
   
   
   
                                     CHAPTER 4
   
                                     REFERENCES
   
   
   
           On G-DIIS:   "Computational  Strategies  for  the  Optimization  of
      Equilibrium    Geometry   and   Transition-State   Structures   at   the
      Semiempirical Level", Peter L.  Cummings, Jill  E.   Gready,  J.   Comp.
      Chem., 10, 939-950 (1989).
   
           On Analytical C.I.  Derivatives:   "  An  Efficient  Procedure  for
      Calculating   the   Molecular   Gradient,   using  SCF-CI  Semiempirical
      Wavefunctions with a Limited  Number  of  Configurations",  M.   J.   S.
      Dewar,  D.   A.   Liotard,  J.   Mol.  Struct.  (Theochem), 206, 123-133
      (1990).
   
           On Eigenvector Following:  J.  Baker,  J.   Comp.   Chem.,  7,  385
      (1986).
   
           On Analytical  C.I.   Derivatives:   "An  Efficient  Procedure  for
      Calculating   the   Molecular   Gradient,   using  SCF-CI  Semiempirical
      Wavefunctions with a Limited  number  of  Configurations",  M.   J.   S.
      Dewar,  D.   A.   Liotard,  J.   Mol.  Struct.  (Theochem), 206, 123-133
      (1990).  On ElectroStatic Potentials  (ESP):   "Atomic  Charges  Derived
      from  Semiempirical  Methods", B.  H.  Besler, K.  M.  Merz, Jr., P.  A.
      Kollman, J.  Comp.  Chem., 11 431-439 (1990).
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
   
                                        4-1
   

   
   
   
                                                             Page Index-1
   
   
                                   INDEX
   
   
   
   +                                   LARGE
     example of, 1-6                     with DRC, 1-8
   &, 2-1                              Learning, 2-2
   +, 2-2                              LOG file, 1-8
                                         introduction, 1-5
   AIDER, 2-2
   AIGIN, 2-3                          MODE=n, 2-5
   AIGOUT, 2-3                         MS=n, 2-6
    
   Band structure, 1-9, 2-5            NOANCI, 2-6
   Brillouin Zones, 2-5                NODIIS, 2-6
                                       NOLOG, 2-6
   C.I., keyword                       NONR, 2-6
     examples of, 1-9                  NOTHIEL, 2-6
                                       NSURF, 2-7
   DEBUG
     redefined, 1-1                    OLDGEO, 2-7
   DIPOLE, 2-3                         One SCF (keyword), 2-2
   DIPX, 2-4                           ORIDE, 2-7
   DIPZ, 2-4
   DMAX=n.n, 2-4                       phonon band structure, 2-5
                                       Phonon spectra, 1-9
   EF, 2-4                             POINT, 2-7
   EIGINV, 2-4                         POINT1=n, 2-7
   Elements                            POINT2=n, 2-7
     labeling, 1-5                     POTWRT, 2-8
   ESP, 2-4                            PRECISE, 1-2
   ESPRST, 2-5                           with FORCE, 1-2
    
   FORCE                               RECALC=n, 2-8
     use of PRECISE, 1-2
                                       SCALE, 2-8
   Gaussian, 1-6                       1SCF, 2-2
   GREEN CROSS CORP, 1-3                 redefined, 1-2
                                       SCFCRT=, 2-8
   Heat of Formation                   SCINCR, 2-8
     Precision, 2-8                    SETUP, 1-2, 2-8
   HESS=n, 2-5                           specification, 1-7
                                       SETUP=name, 2-9
   IUPD=n, 2-5                         SLOPE, 2-9
                                       STEP, 2-9
                                       STO3G, 2-9
   K=(n.nn,n), 2-5                     SYMAVG, 2-9
   KEYWORDS
     redefined, 1-1                    TEKTRONIX, 1-3
   keywords                            TS, 2-9
     priority, 1-7
     specification, 1-7                WILLIAMS, 2-10