CCP6 MOLSCAT User manual
                                Version 12
 
                             Jeremy M. Hutson
 
 
              Department of Chemistry, University of Durham,
        Science Laboratories, South Road, Durham, DH1 3LE, England
 
               Electronic mail: J.M.Hutson @ durham.ac.uk
 
 
                            and Sheldon Green
 
 
      NASA Goddard Space Flight Center, Institute for Space Studies,
                2880 Broadway, New York, NY 10025, U.S.A.
 
             Electronic mail: agxsg@nasagiss.giss.nasa.gov
 
MOLSCAT is a general-purpose package for performing non-reactive molecular
scattering calculations. It is written in near-standard FORTRAN 77, and runs on
(among others) DEC VAX, DEC Ultrix, IBM mainframes, IBM RS/6000, Sun Sparc,
Intel iPSC and CRAY computers. This manual describes the capabilities and modes
of use of the program, and explains the input data required.
 
JMH and SG would be grateful to be informed of any bugs you encounter,
either in MOLSCAT or in this documentation.
 
 
 
 
 
Version of 9 December 1993
 
 
 
 
 
 
 
 
 
                      Table of Contents
 
1. Introduction
   1.0  Acknowledging use of MOLSCAT
   1.1  Collision types
   1.2  Propagators
   1.3  Data format
 
2. NAMELIST block &INPUT
   2.1  General purpose variables
   2.2  Print level control
   2.3  Angular momentum
   2.4  Scattering energies
   2.5  S-matrix output file
   2.6  Partial cross section output file
   2.7  Total cross section output file
   2.8  Propagator scratch file
   2.9  Pressure broadening calculations
   2.10 Characterising scattering resonances
   2.11 Surface scattering calculations
   2.12 Control of propagators
        - Units of length
        - Range of integration
        - Step size
        - DeVogelaere propagator
        - R-matrix propagator
        - Hybrid log-derivative/VIVS propagator
        - WKB propagator
 
3. NAMELIST block &BASIS
   3.1  ITYP = 1
   3.2  ITYP = 2
   3.3  ITYP = 3
   3.4  ITYP = 4
   3.5  ITYP = 5
   3.6  ITYP = 6
   3.7  ITYP = 7
   3.8  ITYP = 8
   3.9  ITYP = 9
   3.10 Decoupling approximations
 
4. NAMELIST block &POTL
   4.1  Exponentials and inverse powers
   4.2  The VSTAR mechanism
   4.3  The VRTP mechanism
 
5. User-supplied potential routines
   5.1  Initialisation
   5.2  Evaluation
 
6. NAMELIST block &CONV
 
7. Array dimensioning
 
8. Subroutines of the MOLSCAT system
 
9. COMMON blocks
 
10. Machine-dependent features
 
11. References
 
 
 
1. Introduction
_______________
 
The outcome of a molecular collision process is described quantum-mechanically
by the S-matrix, which contains information on the probability amplitudes and
phases for the various possible outcomes. Experimental observables, such as
differential and integral cross sections, can be written in terms of S-matrix
elements. For nonreactive collisions a standard computation technique for
solving the time-independent Schrodinger equation involves expanding the
total wavefunction in the (rotation-vibration) basis sets of the colliding
species and a partial wave (spherical harmonic) expansion for the angular
part of the collision coordinate.  This results in coupled second-order
differential equations for radial functions labeled by the quantum numbers
of the asymptotic basis and the partial waves.  The coupling, which vanishes
asymptotically, is due to the intermolecular potential.  Truncation of the
infinite asymptotic basis sets (generally on an energy criterion) leads to the
close-coupling method.  The partial wave sum can be shown to converge if the
potential decreases sufficiently rapidly.  It is generally advantageous to
transform the asymptotic basis set to a total angular momentum representation.
MOLSCAT constructs the coupled equations appropriate to the collision
problem of interest, and then solves these equations to obtain S matrices.
 
Some experimental observables may be calculated directly by invoking particular
options within MOLSCAT. These include
 
 - Elastic and inelastic integral cross sections
 
 - Cross sections for pressure broadening and shifting of spectroscopic lines.
 
Other observables are calculated by separate programs which accept MOLSCAT's
S-matrix output file as input. These include
 
 - Elastic and inelastic differential cross sections
 
 - Generalised effective cross sections for transport and relaxation properties
   (including Senftleben-Beenakker effects)
 
 - Positions and widths of scattering resonances and predissociating states of
   Van der Waals molecules.
 
The data required to invoke these options will be described in detail below.
 
 
1.0 Acknowledging use of MOLSCAT
 
Publications that present results obtained with MOLSCAT should cite it as:
 
J. M. Hutson and S. Green, MOLSCAT computer code, version 12 (1993),
distributed by Collaborative Computational Project No. 6 of the Science and
Engineering Research Council (UK).
 
The date that the program was last updated is usually held in the variable
PDATE in subroutine DRIVER, and is printed out in each run. PDATE is used to
keep track of minor modifications, but the version number is only incremented
when major changes are made.
 
 
1.1 Collision types
 
MOLSCAT can perform close-coupling calculations for the following collision
types, controlled by the &BASIS ITYPE input parameter (see section 3):
 
ITYPE = 1   Atom - linear rigid rotor scattering
 
ITYPE = 2   Atom - vibrating diatom scattering (rotationally and/or
            vibrationally inelastic)
 
ITYPE = 3   Linear rigid rotor - linear rigid rotor scattering
 
ITYPE = 5   Atom - symmetric top scattering (also handles near-symmetric tops)
 
ITYPE = 6   Atom - asymmetric top scattering (also handles spherical tops)
 
ITYPE = 7   A generalised form of ITYPE = 2, allowing the  intermolecular
            potential to depend on the diatom j quantum number
 
ITYPE = 8   Atom - corrugated surface diffractive (elastic) scattering.
            At present, the code is restricted to centrosymmetric lattices, for
            which the potential matrices are real.
 
ITYPE = 9   MOLSCAT calls user-supplied routines to define the coupling case.
 
The computer time required to solve a set of N coupled equations is nominally
proportional to N**3, and in practice the limit on N is from 30 to 500,
depending on the speed of the computer and the amount of memory available. The
basis sets necessary for converged close-coupling calculations quickly exceed
this limit as scattering energies increase or rotational constants decrease,
particularly for collision types 2 to 7. However, MOLSCAT also provides for
various approximate (decoupling) methods which reduce the dimensionality of the
coupled equations. The methods supported at present are
 
IADD = 10   Effective potential approximation
 
IADD = 20   Coupled states (centrifugal sudden) approximation
 
IADD = 30   Decoupled l-dominant approximation.
 
IADD = 100  Infinite order sudden approximation.
 
These approximate methods are invoked by adding the appropriate value of IADD
to the ITYPE values listed above: thus, for example, ITYPE = 22 invokes the
coupled states approximation for atom - vibrating diatom scattering.
 
Not all these approximations are supported for all collision types, though the
most common ones are. The program will print a warning message and exit if you
request an option that is not supported.
 
 
1.2 Propagators
 
The coupled equations may be solved using any one of several methods,
controlled by the input parameter &INPUT INTFLG (see section 2.1).
In the absence of special circumstances, INTFLG = 8 is usually a good choice.
 
INTFLG = 2  DeVogelaere's method. This is a reliable and accurate method, but
            is rather slow, especially for large reduced masses or high
            scattering energies. It is not well suited to problems with very
            long-range potentials.
 
INTFLG = 3  R-matrix propagator. This is a very stable method. It is very
            simple to use, but has relatively poor step size convergence
            properties, so that it is not generally suitable for obtaining very
            high accuracy. It has largely been superseded by the modified
            log-derivative propagators available as INTFLG = 6 to 8 (see
            below).
 
INTFLG = 4  The VIVAS hybrid propagator, using the log-derivative method at
            small R and the variable interval variable step (VIVS) method at
            large R. This is sometimes the most efficient propagator if many
            different energies are required, but control of it is rather more
            complicated than for other propagators. In particular, it requires
            the first and second derivatives of the potential for maximum
            efficiency. It sometimes presents stability problems, and is not
            generally recommended for inexperienced users.
 
            With appropriate choices of the switchover distance, either the
            log-derivative method or VIVS can be used over the whole range of R
            if desired. This will usually be useful only in special cases.
 
INTFLG = 5  Log-derivative propagator of Johnson. This is a very stable and
            reliable propagator, and is particularly efficient on vector
            processors. However, it has now largely been superseded by the
            diabatic modified log-derivative propagator available as INTFLG = 6
            (see below).
 
INTFLG = 6  Diabatic modified log-derivative method of Manolopoulos. This is a
            very efficient and stable method, especially at short range. INTFLG
            = 6 automatically detects single-channel cases (including IOS
            cases) and uses a more efficient implementation of the propagator.
 
INTFLG = 7  Quasiadiabatic modified log-derivative method of Manolopoulos. This
            method offers better accuracy than INTFLG = 6 for very strongly
            coupled problems, but is relatively expensive (even at subsequent
            energies). It is recommended for very strongly coupled problems
            only.
 
INTFLG = 8  Hybrid modified log-derivative Airy propagator of Manolopoulos and
            Alexander. Uses the same method as INTFLG = 6 at short range, but
            changes to the Airy propagator at long range. This is the
            recommended general-purpose propagator for cross section
            calculations.
 
INTFLG = -1 WKB semi-classical solution using Gauss-Mehler quadrature. This is
            suitable only for 1-channel problems and hence is usually useful
            only for IOS (ITYPE.GT.100) cases.
 
Note that Gordon's propagator, which was available as INTFLG = 1 in early
versions of MOLSCAT, is not implemented in this version.
 
All these propagators have options which allow them to use potential matrices
stored at the first total energy when doing calculations at subsequent
energies. For the R-matrix propagator, VIVS, and the modified log-derivative
propagators, some of the remaining work is also avoided at subsequent energies,
so that subsequent energies may cost only 30% as much as the first. For the
DeVogelaere and basic log-derivative propagators the saving in time is much
less spectacular unless the potential is very expensive to evaluate.
 
 
1.3 Data format
 
MOLSCAT's main data file is read on channel 5, and consists of 3 (or 4) blocks
of NAMELIST data:
 
&INPUT, read in subroutine DRIVER
 
&BASIS, read in entry BASIN of subroutine BASE
 
&POTL, read in the initialisation call of subroutine POTENL if the
general-purpose version of POTENL is used (see below).
 
&CONV, read in subroutine CONVRG if the automatic convergence testing option is
selected (ICONV = 1).
 
Each NAMELIST block starts with &<name>, where <name> is INPUT, BASIS, POTL or
CONV as appropriate, and is terminated by &END. Between these delimiters, the
NAMELIST input data consist of "<KEYWORD>=value" entries in the data file,
where <KEYWORD> is the variable name. Note that all lines of data must start in
column 2 or later; characters in column 1 will cause errors. In some
implementations of NAMELIST, every value must be terminated by a comma. Many of
the variables have sensible default values, which are used if the variable is
not listed in the data file.
 
The following sections will describe the variables which can be input in
&INPUT, &BASIS, &POTL and &CONV data, classified according to function.
 
 
2. NAMELIST block &INPUT
________________________
 
 
2.1 General purpose variables
 
LABEL   Title for run (up to 80 characters).
        Note that this must appear in the data file as a literal string
        enclosed in quotation marks, e.g. LABEL='TEST RUN'
 
URED    Reduced mass for collision, m1*m2/(m1+m2), in atomic mass units
        (mass of carbon-12 is 12.0)
 
INTFLG  Selects propagator to be used (see section 1.2 above)
 
LASTIN  (default 1) If LASTIN is set to 1, the run will terminate after the
        current scattering calculation is complete. If LASTIN is 0, another
        complete set of data will be read once this set has been processed.
 
ICONV   (default 0). If ICONV is set to 1 on input, NAMELIST block &CONV will
        be read and the program will perform automatic convergence testing with
        respect to step size, RMIN, RMID or RMAX (see below). If ICONV = 0
        (the default), NAMELIST block &CONV is not read.
 
MXSIG   (default 0). By default, MOLSCAT will accumulate total cross sections
        between every pair of levels in the basis set, including closed
        channels. This uses a fairly large amount of storage, and is often not
        required. If MXSIG is set to a positive integer, only cross sections
        between the first MXSIG levels will be calculated.
 
LMAX, MMAX (default 0). For IOS calculations, these are the highest L and M
        values for which generalized IOS cross sections, Q(L,M,M') will be
        accumulated. For ITYPE=103 (see below), LMAX and MMAX identify the
        maximum L for rotors 1 and 2 respectively.
 
 
2.2 Print level control
 
The amount of printed output produced by MOLSCAT is controlled by the integer
variable PRNTLV; sensible values of PRNTLV vary from 1 (when only total cross
sections are required) to 35 (when debugging). PRNTLV = 3 prints out some
information about each set of coupled equations solved, and complete S-matrices
are printed out if PRNTLV = 11 or more. Voluminous debugging output starts
appearing at PRNTLV = 15.
 
The number of page throws generated is controlled by the parameter ITHROW
(default 0). If ITHROW = 1, each new S-matrix calculation starts on a new page.
 
The printing of total and partial cross sections is controlled by the parameter
ISIGPR (default 0). This must be set to 1 if printing of cross sections is
required.
 
 
2.3 Angular momentum
 
MOLSCAT has built-in loops over total angular momentum JTOT and symmetry types
M. The loop over JTOT is controlled by the three input variables JTOTL, JTOTU
and JSTEP; the program will loop from JTOTL to JTOTU in steps of JSTEP. Note
that the orbital angular momentum label appearing in various decoupling schemes
is treated as a total angular momentum for this purpose.
 
If total cross sections are required, there is an alternative form of input
flagged by the value JTOTU .GE. 999 (or JTOTU .LT. JTOTL). The end of the loop
over JTOT is then controlled by the variables DTOL, OTOL and NCAC: JTOT will
start at JTOTL and be incremented by JSTEP until NCAC successive JTOT values
each contribute less that DTOL to any diagonal cross section matrix element and
less than OTOL to any off-diagonal matrix element. This option should be used
with care, since you must be sure that the calculation will converge before the
job runs out of time. Note that elastic cross sections usually converge very
much more slowly than inelastic ones.
 
The loop over symmetry types ("parity cases") M is used differently for
different decoupling schemes. For close-coupling, M takes values 1 and 2 for
odd and even parity label respectively. For coupled states calculations, M-1 is
the body-fixed projection quantum number. Under normal circumstances, MOLSCAT
loops over all possible values of M for the coupling case concerned. However,
if the input variable MSET is non-zero (default 0), MOLSCAT will skip all
calculations except for M=MSET. This option is particularly useful for
resonance searches (see section 2.10) and convergence checking (see section 5).
If MHI is also non-zero, calculations are performed for the range of M values
from MSET to MHI.
 
 
2.4 Scattering energies
 
The total energies at which scattering calculations are performed are
controlled by the array ENERGY and the variables NNRG, NTEMP, TEMP, DNRG and
EUNITS. If DNRG = 0.0 (the default), calculations will be performed for the
NNRG energies listed in the ENERGY array. If DNRG is not 0.0, calculations will
be performed at NNRG equally spaced energies, DNRG apart, starting at ENERGY(1).
The maximum allowed value of NNRG is currently 100.
 
The units of ENERGY and DNRG are determined by the integer variable EUNITS
(default 1) as follows:
 
      EUNITS = 1     1/cm
      EUNITS = 2     Kelvin
      EUNITS = 3     MHz
      EUNITS = 4     GHz
      EUNITS = 5     eV
      EUNITS = 6     erg
      EUNITS = 7     Hartrees
      EUNITS = 8     kJ/mol
      EUNITS = 9     kcal/mol
 
If a character string is input to EUNITS (not allowed on some machines), an
attempt is made to match one of the allowed units and set the conversion
factor.
 
The input energies are converted immediately into 1/cm using the appropriate
conversion factor, and all energies subsequently printed by MOLSCAT are in 1/cm.
 
There are special interpretations of the NNRG and ENERGY parameters which may
be invoked when
 
1) Searching for resonances
2) Calculating line broadening cross sections.
 
These are described separately in the appropriate sections below.
 
An alternative form of input is available to facilitate Boltzmann averaging of
cross sections using Gaussian quadrature. This is controlled by the array TEMP
and the variables NTEMP and NGAUSS. If NTEMP is greater than 0 (default 0),
scattering calculations are performed at energies corresponding to NGAUSS point
Gaussian quadratures for the NTEMP different temperatures (in Kelvin) in the
TEMP array. The maximum allowed values are NTEMP = 5 and NGAUSS = 6. Note that
Gaussian quadrature is not a very reliable way of thermally averaging some
types of cross sections, and use of this option is generally not recommended.
 
 
2.5 S-matrix output file
 
In addition to its main printed output on channel 6, MOLSCAT can also write
out a file containing S-matrices for subsequent processing by another
program (for example, in the calculation of differential cross sections or
transport/relaxation cross sections). This option is invoked if ISAVEU is not 0
(default 0), and the S-matrices are then written to channel ISAVEU.
 
Early versions of the program saved this in formatted card image files with
format statements as indicated below. From MOLSCAT version 11 onwards (June
92), the data are saved in unformatted (binary) files which provide better
precision, use less space, and reduce the conversion overhead. In the binary
files the data enumerated below are written in the same order, as single
(logical) records (i.e. single unformatted WRITE statements), except for (7),
which is described more fully below.
 
The format of the file produced is as follows:
 
  1.) LABEL,ITYPE,NLEV,NQN,URED,IP (A80/3I4,F8.4,I4)
      LABEL = title of run.
      ITYPE specifies the collision type.
      NLEV is the number of levels in the angular basis set.
      NQN is the number of (quantum) descriptors per level.
      URED is the reduced mass in atomic mass units.
      IP is the MOLSCAT version number (12 in this version).
 
  2.) ((JLEV(I,J),I=1,NLEV),J=1,NQN)  (20I4)
      JLEV(ILEV,J) are the quantum numbers of level ILEV.
      The meaning depends on ITYPE.
 
  3.) NLEVEL,(ELEVEL(I),I=1,NLEVEL)  (I4/(5E16.8))
      Number and values of the asymptotic level energies (1/cm).
 
  4.) NNRG,(ENERGY(I),I=1,NNRG)  (I4/(5E16.8))
      Number and values of the scattering energies (1/cm).
 
  5.) JTOT,INRG,EN,IEXCH,WT,M  (2I4,E16.8,I4,E16.8,I4)
      These describe a single scattering calculation:
      JTOT is the total angular momentum.
      INRG is the index of the energy in the list in 4.).
      EN is the total energy (1/cm).
      IEXCH is the exchange parity for identical molecules
          IEXCH = 0: no exchange symmetry
          IEXCH = 1: odd exchange symmetry
          IEXCH = 2: even exchange symmetry
      WT is the statistical weight of this JTOT, M.
      M is the serial index of the symmetry block.
 
  6.) NOPEN,(LEV(I),L(I),WV(I),I=1,NOPEN)  (I4/(2I4,E16.8))
      NOPEN is the number of open channels in the S-matrix.
      LEV(I) is the index of JLEV in 2.) for channel I.
      L(I) is the orbital angular momentum for channel I.
      WV(I) is the wavevector of channel I (1/Angstroms).
 
  7.) (SREAL(I),I=1,NSQ),(SIMAG(I),I=1,NSQ)  (5E16.8)
      NSQ=NOPEN*NOPEN
 
      SREAL(I) and SIMAG(I) are the real and imaginary parts of the S-matrix
      elements, listed in FORTRAN storage order for the NOPEN*NOPEN matrices
      SREAL and SIMAG. In unformatted files (version 11 and later), SREAL and
      SIMAG are each written as a single record, listing only the lower
      triangle, i.e.
 
      ((S(I,J),J=1,I),I=1,NOPEN)
 
      These arrays are written by calls to subroutine SWRITE, and entry SREAD
      in that routine can be used for read the records for subsequent
      processing.
 
      5.), 6.) and 7.) are repeated for each S-matrix calculated, looping over
      INRG (innermost), M and JTOT (outermost):
 
      JTOT = JTOTL,JTOTU,JSTEP
      M = 1,MXPAR
      INRG = 1,NNRG
      5.), 6.), 7.)
      END LOOP
 
      MXPAR depends on ITYPE. Note that not every S-matrix will necessarily
      exist. S-matrices may be missing from the file either because there are
      no open channels for that energy, or because there was an error or
      convergence failure in the calculation.
 
      The S-matrix output file is not supported for IOS calculations, and the
      output that can be generated for some cases is probably not generally
      useful.
 
 
2.6 Partial cross section output file
 
The option to write out partial cross sections to a separate file is not
implemented in this version of MOLSCAT, but could be resuscitated if necessary.
 
 
2.7 Total cross section output file
 
If ISIGU is greater than 0 (default 0), MOLSCAT will maintain a (direct access)
file containing accumulated cross sections on channel ISIGU. This file is
updated after each complete JTOT, so it contains valid information about the
run so far even if the program terminates abnormally.
 
 
2.8 Propagator scratch file
 
All the propagators have options to save energy-independent matrices on a
scratch file to save computation at subsequent energies. This is particularly
advantageous for the R-matrix and VIVS propagators. If ISCRU is greater than 0
(default 0), this save file is created on channel ISCRU and used for any
subsequent energies. It can be very large.
 
Note that this option saves CPU time at the expense of disc i/o. It is usually
advantageous for the R-matrix, VIVS, quasiadiabatic and hybrid Airy propagators
if NNRG is not 1, but for the DeVogelaere and basic log-derivative propagators
it may not save resources overall unless the potential itself is very expensive
to calculate. This is particularly true on fast machines such as CRAYs. Note,
however, that ISCRU > 0 saves considerable time for single-channel IOS cases
with INTFLG=6, since the computer time for these is usually dominated by
potential evaluations.
 
When searching for and characterising resonances, a propagator scratch file
created in one run may be used in a subsequent run to save work. This is
described in section 2.10 below.
 
The propagator scratch file option is not implemented in the parallel version
of MOLSCAT.
 
 
2.9 Pressure broadening cross sections
 
Calculations of pressure broadening and shifting cross sections are supported
for ITYPE = 1, 2, 3, 5, 6, 7, 11, 12, 15, 16, 17, 21, 22, 25, 26, 27, 31, 101,
and 105. The pressure broadening option is invoked if NLPRBR is greater than 0
on input (default 0); the value of NLPRBR specifies the number of spectroscopic
lines for which pressure broadening calculations are to be carried out. The
lines themselves are specified by the array LINE, of 4*NLPRBR elements. Each
successive quartet of elements of LINE indexes the rotor levels involved in the
transition, according to the elements of the JLEVEL array described in section
3. The 4 values indicate JA, JB, JA', JB' where JA->JB is the spectroscopic
transition and the primes indicate post-collision values. Note that the
"diagonal" values JA=JA' and JB=JB' describe widths and shifts of isolated
lines, and off-diagonal values describe collisional transfer of intensity.
 
Pressure broadening calculations require S-matrix elements involving the
initial and final (spectroscopic) levels at the same kinetic (not total)
energy. Generation of the necessary total energies is facilitated by the input
parameter IFEGEN. If IFEGEN is set to 1 (default 0), the program will treat the
input ENERGY values as kinetic energies, and generate the necessary total
energies for the lines requested. If IFEGEN is 0, only those requested lines
which can be constructed from the total energies actually specified by
NNRG,ENERGY will be calculated.
 
The tensor order of the spectroscopic transition (e.g. 1 for dipole
transitions, 0 for isotropic Raman scattering) is specified in the input array
LTYPE. If the default value (-1) is found, LTYPE is calculated from ABS(JA-JB).
 
 
2.10 Characterising scattering resonances
 
Scattering resonances and predissociating states of Van der Waals molecules
appear as characteristic features in the energy-dependence of S-matrices. In
MOLSCAT, a run to find or characterise a resonance is flagged by setting the
parameter KSAVE > 0 (default 0). This option is NOT supported for IOS
calculations (ITYPE > 100). Setting KSAVE > 0 has principal effects:
 
1) The S-matrix eigenphase sum is calculated at each energy, and a short
   summary of the eigenphase sums is written to channel KSAVE.
 
2) The output to channel ISAVEU is modified to be suitable for use with the
   program RESFIT. S-matrices, K-matrices and eigenphase sums are written to
   channel ISAVEU unformatted.
 
A MOLSCAT run to characterise a resonance must deal with only one total angular
momentum JTOT and symmetry type M in a given run. Thus, JTOTL and JTOTU must be
the same, and the parameter MSET must be set greater than 0 to select the
particular symmetry type required.
 
A special option is available to assist with searching for narrow resonances.
If NNRG is given as a negative integer of the form -5*N, with N integral and
the energies themselves specified by ENERGY(1) and DNRG, MOLSCAT will perform N
groups of 5 equally spaced calculations. After each group, the program will try
to interpret the 5 eigenphase sums as the "tail" of a resonance, and estimate
the position of the resonance centre. This estimate is then used as the
starting point for the next group of 5 energies. This option can be useful in
searching for a resonance if a reasonably good estimate of its energy is
already available, and may succeed in converging on a narrow resonance from as
far as 10**5 widths away. However, convergence is NOT guaranteed, and it is not
usually useful to do more than 3 sets of 5 energies in a single run.
 
Resonance search calculations should usually be done with either the R-matrix
propagator or one of the modified log-derivative propagators, since many
different energies are always necessary. It is thus always desirable to use the
ISCRU option to save energy-independent matrices on a scratch file. For the
special case of resonance searches, with JTOTU = JTOTL and MSET > 0, the ISCRU
file from one run may be used as input for the next run at a different set of
energies. This option is invoked by setting ISCRU negative for the subsequent
run(s); the program then expects to find a suitable input file on channel
|ISCRU|. It reads the header on this file to check that it contains valid
information, and then proceeds with "subsequent energy" calculations for all
the energies requested.
 
 
2.11 Surface scattering calculations
 
Atom - surface scattering calculations are not plagued by complications arising
from total angular momentum and parity. MOLSCAT uses the internal loops over
JTOT and M to loop over the polar angle theta (measured from the surface
normal) and the azimuthal angle phi (measured relative to the surface
reciprocal lattice vector g1). The loop over theta is controlled by the input
parameters JTOTL, JTOTU, JSTEP, THETLW and THETST, while that over phi is
controlled by MXPHI, PHILW and PHIST. The logic used is equivalent to:
 
      DO 840 JTOT = JTOTL,JTOTU,JSTEP
      THETA = THETLW + THETST*JTOT
      DO 830 M = 1,MXPHI
      PHI = PHILW + PHIST*(M-1)
      ..
      ..
      Scattering calculation for angles THETA, PHI
      ..
      ..
  830 CONTINUE
  840 CONTINUE
 
Note that, for surface scattering, subsequent energies have a rather
non-intuitive meaning, because the threshold energies (K+G)**2 depend on the
parallel component of the momentum K. MOLSCAT interprets subsequent energies as
having the SAME parallel momentum as the first energy, but a different
perpendicular momentum. This corresponds to a change in the polar angle as well
as the scattering energy.
 
 
2.12 Control of propagators
 
Convergence of coupled channel calculations with respect to integration range
and step size is very important; lack of convergence can give very poor
results, whereas unnecessarily conservative tolerances can waste large amounts
of computer time. It is always advisable to conduct careful step size
convergence tests on a small basis set before embarking on any major set of
calculations with MOLSCAT.
 
Units of length
_______________
 
MOLSCAT operates with units of lengths specified by RM, which is set in
subroutine POTENL (see section 5) and which may be input via the &POTL data set
(see section 4). Variables which control the integration, such as RMIN, RMAX,
etc. (described below) are in units of RM. Note that RM itself is specified in
units of Angstroms, and users might find it convenient to have all distances in
Angstroms by setting RM=1.0.  As another example, to specify all distances in
bohr radii (atomic units) one should specify RM=0.529177.
 
Range of integration
____________________
 
The mechanisms used to choose the starting and finishing points for integrating
the coupled equations are the same for all propagators. In the simplest case,
the input variables RMIN (default 0.8) and RMAX (default 10.0) are supplied and
used exactly as input. However, in certain circumstances this behaviour is
modified:
 
1) If IRMSET > 0 on input (default 9), the program will estimate a suitable
   distance to start propagating, using the criterion that the wavefunction
   amplitude in all channels should be less than 10**(-IRMSET) at the starting
   point. A crude semiclassical estimate of the wavefunction is used to make
   this estimate, which is calculated separately for each JTOT, M (at the first
   energy only).
 
2) If there is a centrifugal barrier present, the program checks that all open
   channels are classically accessible at the RMAX requested, for all energies
   in the ENERGY list. If necessary, RMAX is increased to the value of R at the
   furthest classical turning point found in the centrifugal potential for any
   energy. However, RMAX is never decreased from the input value.
 
   For special purposes, this action can be suppressed by setting IRXSET = 0 on
   input (default 1). However, this is not recommended for general cross
   section calculations.
 
   Thus, the input value of RMAX is the smallest distance at which the
   propagator may terminate. The DeVogelaere and R-matrix propagators also
   check some aspects of convergence internally, and may propagate beyond RMAX
   under certain circumstances.
 
   It should be noted that propagating out to the centrifugal turning point is
   NOT necessarily adequate, particularly when calculating elastic integral
   cross sections or line shift cross sections. It is also important to realise
   that a value of RMAX which is adequate for low JTOT may not be adequate for
   high JTOT, and that calculations using too small a value of RMAX may appear
   to be converged with respect to the partial wave sum when they are not
   actually converged.
 
Step size
_________
 
The DeVogelaere and the basic log-derivative propagators are
wavefunction-following methods, and use a constant step size controlled by the
parameter STEPS (default 10.0). This is interpreted as the number of steps per
half-wavelength for the open channel of highest kinetic energy in the
asymptotic region. A value between 10 and 20 is usually adequate, unless the
depth of the potential well is large compared to the scattering energy.
 
The two modified log-derivative propagators are actually potential-following
methods, but they nevertheless use the same mechanism (STEPS) to determine step
size, for compatibility with the basic log-derivative code. For these
propagators, values of STEPS around 5.0 are usually adequate.
 
The R-matrix and VIVS propagators are potential-following methods, so the de
Broglie wavelength is less important. Instead, the required initial step size
is input explicitly in the variable DR (default 0.02). However, in both
propagators the step size may subsequently be modified, as described for the
individual propagators below.
 
DeVogelaere propagator (INTFLG = 2)
______________________
 
STABIL   The DeVogelaere method is potentially unstable in a classically
         forbidden region, because the exponential growth of closed channel
         wavefunctions can lead to a loss of linear independence of the
         solutions. To avoid this, the DeVogelaere propagator re-imposes linear
         independence every STABIL steps. The default (5.0) is usually
         adequate.
 
STEST    is an integration tolerance parameter used for two purposes:
 
         1) The K-matrix obtained by matching to the asymptotic boundary
            conditions should be exactly symmetric, but this is never the case
            because of numerical rounding errors. The program counts and prints
            out the number of pairs of symmetry-related off-diagonal elements
            which differ by more than STEST.
 
         2) The S-matrix is calculated at successive values of R, starting at
            RMAX and incrementing by approximately half a wavelength each time.
            This is repeated until two successive S-matrices differ by no more
            than STEST in any element, up to a maximum of 20 attempts.
 
R-matrix propagator (INTFLG = 3)
___________________
 
RMID     (default 9999.0). For R < RMID, the R-matrix propagator uses a
         constant step size of DR. For R > RMID, the step size is DR*R/RMID, so
         that larger steps are taken in the long-range region. If RVFAC is set
         greater than the default value of 0.0, RMID is set automatically to
         RVFAC*RTURN, where RTURN is an estimate of the position of the
         classical turning point, calculated for each JTOT and parity case.
 
SHRINK   If the integer variable SHRINK is 1 on input (the default), the
         R-matrix propagator will monitor closed channels in the long range
         region and accumulate a phase integral for each. If a semiclassical
         estimate based on this phase integral indicates that the wavefunction
         amplitude in the channel concerned has dropped below 10**(-IRMSET),
         the channel will be removed from the basis set for the remainder of
         the propagation.
 
VTOL     controls a convergence criterion applied to the eigenvectors of the
         potential matrix (default VTOL = 1.D-6). The R-matrix propagator will
         not attempt to apply boundary conditions until the eigenvector is a
         (permuted) unit matrix to within tolerance VTOL for two successive
         steps. This test is applied only to eigenvectors which are
         asymptotically non-degenerate.
 
MAXSTP   is the largest number of steps allowed for the R-matrix propagator
         (default 10000). If convergence has not been achieved after this many
         steps, the program prints an error message and exits.
 
Hybrid log-derivative/VIVS (VIVAS) propagator (INTFLG = 4)
_____________________________________________
 
RVIVAS   (default 9999.0) is the distance at which the switchover from the
         log-derivative method to VIVS takes place (but see also RVFAC below).
         A value of RVIVAS just inside the potential minimum is usually most
         efficient. If RVIVAS is more than RMAX, the entire propagation will
         use the log-derivative method; however, the preferred method of
         achieving this effect is to use INTFLG = 5, since this uses
         considerably less storage. Conversely, if RVIVAS is less that RMIN,
         the entire propagation will use VIVS (not recommended). It must be
         remembered that MOLSCAT itself may adjust RMIN and RMAX as described
         above; RVIVAS can if necessary be set to a large negative or positive
         number to ensure the desired effect.
 
RVFAC    (default 0.0). If RVFAC > 0.0, RVIVAS (and RMID) is adjusted
         automatically for each JTOT / parity case, to be RVFAC times an
         estimate of the classical turning point. A value of RVFAC around 1.1
         is usually suitable, and is recommended for cross section calculations
         using INTFLG = 4.
 
The log-derivative propagator has no variable parameters except STEPS, which
determines the step size as described above. However, control of the VIVS
propagator is quite complicated. VIVS operates with both a variable interval
length and a variable step length. A single diagonalising transformation is
used over the whole of each interval, which may consist of several steps. The
algorithms used to determine interval and step sizes will be discussed
separately.
 
The step size and interval size algorithms used by VIVS attempt to take the
longest step which will give the required accuracy at each point in the
integration. However, the optimum step size at one scattering energy is not
necessarily safe at another, and VIVS can sometimes give problems if the groups
of energies in a particular run are not chosen with care. In particular, one
should avoid: 1) A first energy which is close to (or above) a channel
threshold and a subsequent energy which is far below it. 2) A first energy
which is far above a channel threshold and a subsequent energy which is close
to it.
 
1) Interval sizes
 
TOLHI    VIVS accumulates perturbation corrections to the wavefunction as it
         propagates, and uses these to obtain a suitable length for the next
         interval. The input parameter DR described above is used as the size
         of the first interval, and subsequent interval lengths are obtained
         using the input tolerance TOLHI (default 0.001); the criterion is that
         some functional t of the perturbation corrections should be not
         greater than TOLHI over any interval. Within an interval, t is checked
         against TOLHI at each step, and a new interval is started (with a new
         diagonalising transformation) if it appears likely to exceed TOLHI
         over the next step.
 
2) Step sizes
 
Each interval is divided into IALPHA steps (default IALPHA = 6). Within an
interval, the step sizes increase geometrically, with each step being a factor
alpha larger than the previous one. The quantity alpha may be specified in
either of 2 ways:
 
i)  If the logical input parameter IALFP is .FALSE. (the default), alpha
    increases linearly from ALPHA1 (default 1.0) at the starting point for VIVS
    to ALPHA2 (default 1.5) at RMAX.
 
ii) If IALFP is .TRUE. on input, the program starts with an initial value of
    ALPHA1, and adjusts this as it propagates. ALPHA2 is then not used.
 
3) Automatic step and interval lengths
 
A useful special option is obtained by setting IALPHA = 0 on input. Intervals
then consist of a variable number of steps, and the decision to start a new
interval is based solely on the magnitude of the perturbation corrections; a
new interval is started (and a new diagonalising transformation obtained)
whenever the quantity t approaches TOLHI. The initial step size is taken from
DR, and subsequent steps use a criterion based on TOLHI.
 
The IALPHA = 0 option can be very efficient, and often requires remarkably few
intervals/steps to produce converged results.
 
4) Perturbation corrections
 
There are several logical input variables which control the extent to which
VIVS calculates and uses perturbation corrections to the wavefunction. The
three variables IV, IVP and IVPP (defaults .TRUE., .FALSE. and .FALSE.
respectively) control the calculation of perturbation corrections due to the
potential itself (IV) and to its first (IVP) and second (IVPP) derivatives. The
perturbation corrections thus calculated are used in calculating interval
sizes, but are included in the wavefunction only if IPERT is .TRUE. (the
default). If ISHIFT is .TRUE. (default .FALSE.), the second derivative is used
to shift the reference potential to give the best fit to the true potential.
 
For production runs, IV, IVP, IVPP, IPERT and ISHIFT should usually all be
.TRUE. This may be forced by setting IDIAG = .TRUE., which overrides any
.FALSE. values for the individual variables.
 
If IVP, IVPP or ISHIFT is set, VIVS will require radial derivatives of the
potential. These are supplied properly for simple potentials by the standard
version of POTENL described below, but for some potentials they can be
difficult to evaluate. In this case, the input variable NUMDER may be set
.TRUE., in which case the necessary derivatives are calculated numerically, and
POTENL is never called with IC > 0 (see section 5).
 
5) Other variables
 
ISYM     (default .TRUE.). If ISYM is .TRUE., the R-matrix is forced to be
         symmetric at the end of each interval. This is usually advisable for
         production runs.
 
XSQMAX   (default 1.E4) controls the application of perturbation corrections to
         deeply closed channels. If a channel is locally closed by more than
         XSQMAX reduced units, perturbation corrections for it are not
         calculated. The default should be adequate.
 
 
Log-derivative propagators (INTFLG = 5, 6 and 7)
_________________________
 
The only relevant input variables are RMIN, RMAX and STEPS as described at the
beginning of this section.
 
 
Hybrid log-derivative/Airy propagator (INTFLG = 8)
_____________________________________
 
The modified log-derivative (INTFLG = 6) propagator is used from RMIN to RMID.
In general, values of RMID somewhat beyond the distance of the minimum are
recommended.  If RVFAC > 0.0 on input, RMID is calculated as described
above; values of 1.2 to 1.4 are generally useful. If RMID is less than RMIN,
or if it is determined that RMID-RMIN is smaller than one step, the
log-derivative propagator will be skipped.  The step size for this propagator
is controlled by STEPS as described above unless IABSDR (default 0) is set to
1, in which case the step size is taken from the input DR.
 
The Airy propagator is used to propagate from RMID to RMAX. If RMID is greater
than RMAX this propagator is not called. By default the initial step size is
taken as the value calculated for the modified log-derivative part, but it
can be further controlled by the following variables.
 
DRAIRY   (default -1.0) can be used to input an absolute step size.
         If DRAIRY is less than zero, the initial step size is taken
         from the log-derivative propagator.
 
TOLHI    (default 0.001). If less than 1, the propagator uses this as a
         tolerance to adjust the step size (by a perturbation method) to try to
         maintain this accuracy. If greater than 1, the step size is increased
         by this factor in each interval.  Values around 1.03 to 1.07 are
         generally useful.
 
POWRX    (default 3). If TOLHI is less than 1, this is the inverse power used
         in estimating the step size from perturbation calculations. The
         default value is usually adequate.
 
WKB propagator (INTFLG = -1)
__________________________________________________
 
The INTFLG=-1 propagator is suitable only for single channel cases and is
used almost exclusively for IOS calculations.  It does the WKB integral
for the phase shift by Gauss-Mehler quadrature as suggested by Pack, J. Chem.
Phys. 60, 633 (1974).  It is  controlled by input variables NGMP and TOL
 
NGMP     Dimension 3.  N-point Gauss integration is done starting
         with N = NGMP(1), incrementing by NGMP(2), until NGMP(3).
         Starting with the 2nd pass the phase shift is compared
         with the previously calculated value until it has
         converged to within a tolerance specified by TOL.
 
TOL      (default = 0.001) is the convergence tolerance for the
         WKB phase shift.
 
 
 
3. NAMELIST block &BASIS
________________________
 
The parameters input in &BASIS specify the collision type, the quantum numbers
and energies of the levels to be used in the basis set, and the dynamical
approximations (if any) to be used in constructing the coupled equations. The
input parameters common to all collision types are as follows:
 
ITYPE    specifies the collision type, as described in section 1.1. It is
         constructed from ITYP, which specifies the nature of the colliding
         particles, and IADD, which specifies the dynamical approximations to
         be made (if any). The values allowed for ITYP are as follows:
 
         ITYP = 1  Linear rigid rotor + atom.
         ITYP = 2  Diatomic vibrotor + atom.
         ITYP = 3  Linear rigid rotor + linear rigid rotor.
         ITYP = 5  Symmetric top rigid rotor + atom.
         ITYP = 6  Asymmetric rigid rotor + atom.
         ITYP = 7  Diatomic vibrotor + atom, with different diagonal potentials
                   for different rotational levels.
         ITYP = 8  Atom + rigid corrugated surface.
 
         Approximate methods are specified as follows:
 
         ITYPE = ITYP       Full close-coupling
         ITYPE = ITYP + 10  Effective potential method
         ITYPE = ITYP + 20  Coupled states approximation
         ITYPE = ITYP + 30  Decoupled l-dominant approximation
         ITYPE = ITYP + 100 Infinite order sudden approximation
 
NLEVEL   If NLEVEL > 0, it is the number of levels to be included in the basis
         set, as specified by the JLEVEL array.
 
         If NLEVEL = 0, the quantum numbers for the levels to be included in
         the basis set will be calculated internally as described for the
         individual collision types below.
 
JLEVEL   is an integer array specifying the quantum numbers of the levels to be
         included in the basis set. The JLEVEL array is structured differently
         for different values of ITYP as described below. JLEVEL is a one-
         dimensional array of dimension 400, although it is conceptually
         two-dimensional for ITYP > 1.
 
ELEVEL   is an array of NLEVEL molecular level energies, corresponding to the
         levels in the JLEVEL array. If all the elements of ELEVEL are 0.0, or
         NLEVEL is 0, the energies are calculated using molecular constants as
         described below, and ELEVEL is not used. ELEVEL is currently
         dimensioned at 200.
 
EUNITS   is an integer specifying the energy units for ELEVEL and molecular
         constants input in &BASIS. EUNITS is interpreted in the same way as
         the EUNITS parameter of the &INPUT NAMELIST block (see section 2.4).
 
The parameters used to control the automatic generation of basis sets and
energy levels from quantum numbers and molecular constants will be described
separately for the different values of ITYP below. The methods of specifying
the molecular levels to be included are independent of any dynamical
approximations employed, so that the information given for each ITYP below is
applicable to ITYPE = ITYP, ITYP+10, ITYP+20 and ITYP+30. For IOS cases (ITYPE
= ITYP+100) the required input is generally the same, except that rotational
level energies are not required for IOS calculations.
 
 
3.1 ITYP = 1
 
For atom - linear rigid rotor systems, the JLEVEL array is usually generated
from input parameters JMIN, JMAX and JSTEP, which have the obvious meanings.
For special purposes, NLEVEL may be set greater than zero and a list of NLEVEL
j values supplied in the array JLEVEL.
 
If JLEVEL is calculated from JMIN, JMAX and JSTEP, the energy levels are
generated from the input parameters BE (rotational constant), ALPHAE
(vibrational dependence of BE), and DE (centrifugal distortion constant). The
rotational constant actually used is of course simply BE-0.5*ALPHAE, and this
value may be input directly in BE with ALPHAE = 0.0 (the default) if preferred.
 
If NLEVEL .GT. 0, the energy levels may be specified in the input array ELEVEL.
If ELEVEL is not supplied, they are generated from BE etc. as above.
 
 
3.2 ITYP = 2
 
For atom - vibrating diatom scattering, the JLEVEL array must contain a list of
(j,v) pairs specifying the rotational and vibrational quantum numbers of the
levels to be included in the basis set. There is no option for generating this
list automatically.
 
If the level energies are not supplied in ELEVEL, they are generated from the
input parameters WE (omega(e)), WEXE (omega(e)x(e)), BE (rotational constant)
and ALPHAE (alpha(e)), using the standard formulae. DE is not used for ITYP =
2. Note that energies calculated from WE, etc. are set with the zero of energy
at v = j = 0.
 
For IOS calculations, the vibrational quantum numbers are selected from the
JLEVEL array, and any rotational quantum numbers supplied are ignored. If
vibrational energies are supplied in ELEVEL, the first one encountered for each
vibrational state is kept. If all ELEVEL are zero, energies are generated from
WE and WEXE.
 
If the input NLEVEL is negative, a user-supplied routine GET102 is called to
set NLEVEL, JLEVEL and ELEVEL values.
 
 
3.3 ITYP = 3
 
For linear rigid rotor - linear rigid rotor scattering, the JLEVEL array must
contain a list of (j1,j2) pairs describing the rotational quantum numbers of
the two molecules. If NLEVEL = 0 on input, JLEVEL is generated from J1MIN,
J1MAX, J1STEP, J2MIN, J2MAX and J2STEP, which have the obvious meanings for
molecules 1 and 2 respectively.
 
If the two molecules are identical, the basis functions corresponding to
(j1,j2) and (j2,j1) are indistinguishable. In this case, the input variable
IDENT (default 0) should be set to 1. Only distinguishable pairs (i.e. J1 .GE.
J2) should be supplied. It is also necessary to specify the statistical weights
to be applied to the different symmetry combinations when calculating cross
sections. The statistical weights for anti-symmetric and symmetric
combinations of (j1,j2) and (j2,j1) may either be specified explicitly in the
WT array as WT(1) and WT(2) respectively, or (if both WT(1) and WT(2) are zero)
may be calculated from the single nuclear spin input in SPNUC. Note that
MOLSCAT will not perform a scattering calculation for any symmetry type with a
statistical weight of zero.
 
Energy values may be specified in ELEVEL or (if all ELEVEL are zero) will be
computed from BE(I), ALPHAE(I) and DE(I). If IDENT=1 and the values for I=2 are
zero, the program sets them equal to the values for I=1.
 
 
3.4 ITYP = 4
 
Not used in this version of MOLSCAT
 
 
3.5 ITYP = 5
 
Rotor basis sets may be taken either from NLEVEL, JLEVEL input or from quantum
number restrictions. In the former case, NLEVEL should be greater than 0 and
rotor levels should be specified in JLEVEL(3*i-2)=j, JLEVEL(3*i-1)=k, and
JLEVEL(3*i)=parity, i=i,NLEVEL. Note that parity is indicated by an even or an
odd integer for even and odd combinations of (+k) and (-k); for k=0, only even
parity is allowed.
 
Alternatively, the basis set may be specified as including levels for j from
JMIN to JMAX: JSTEP is not used. The additional input variable KSET (default 0)
may be used to limit the k values included: if KSET is negative, only levels
with k=|J2MAX| are included; if KSET is zero or positive, only levels with k
less than or equal to KSET are included. If ALL k levels are required, KSET
should be set to at least JMAX (999 recommended).
 
The corresponding energy levels may either be input in ELEVEL, or they may be
calculated from the zeroth order near-symmetric top equation using rotational
constants supplied in the input variables A, B and C. Note that these MUST
correspond, respectively, to moments of inertia about the x, y, and z axes used
in the description of the potential (see below); they may not be in the
descending order standardly adopted in spectroscopy. In particular, the program
requires that the z axis be the symmetry axis of the top (or the axis of near
symmetry) and that the x-z plane be a reflection plane. For a symmetric top,
then, A=B and C is the unique constant.
 
 
3.6 ITYP = 6
 
Asymmetric top wavefunctions are expanded in terms of symmetric top functions.
The necessary functions may either be calculated internally or supplied as
data. If NLEVEL is 0 and all three of A, B and C are specified, the program
constructs the asymmetric top Hamiltonian and diagonalises it. Note that (as
for ITYP=5) A, B and C MUST correspond to the x, y and z axes used in the
potential expansion, and are NOT necessarily in descending order of magnitude.
 
Alternatively, the program (subroutine SET6) may obtain the wavefunctions by
reading data from unit IASYMU (specified in &BASIS, default = 5, the standard
input unit). If IASYMU is the standard input unit, data cards should follow the
&BASIS ... &END set and precede the &POTL set. If NLEVEL is set in &BASIS, this
number of rotor descriptions will be expected. (If IASYMU is an auxiliary unit,
it may be convenient to read levels until an end-of-file condition occurs.)
Each level is described by J,ITAU,ELVL (2I5,F15.10) where J is the rotational
quantum number, ITAU is an index that is not actually used, and ELVL is the
rotor energy (in 1/cm unless &BASIS EUNITS has specified otherwise). For
each level, NK=2*J+1 expansion coefficients are required (corresponding to
k=-J,-J+1,...,+J) and these must follow the J,ITAU,ELVL card in format (6F12.8)
on (NK+5)/6 subsequent cards. Coefficients need not be normalized, but they
will be checked for valid symmetries (by subroutine IPASYM). Note that the
coefficients must correspond to symmetric top functions in the coordinate
system of the potential energy (cf. ITYP = 5 above); in particular, the
rotational constants used to diagonalize the rotor hamiltonian must correspond
to the x, y, and z-axes in which the potential is described.  Note that for
IOS calculations (ITYPE = 106) generation of rotational wavefunctions from the
rotaitonal constants is not supported and they must be explicitly supplied as
data.
 
Asymmetric top functions are characterised by two symmetries:
 
(1) the k values involved are EITHER even OR odd (corresponding to + or -
    symmetry with respect to a C2 rotation about the z axis)
(2) the functions are of the form
         sum_k c_k (D_mk + epsilon D_m,-k)
    where epsilon is either +1 or -1.
 
Internally, the program assigns one of four symmetry types to each asymmetric
top function (in subroutine IPASYM):
 
   PRTY      even/odd k        epsilon
     0          even             +1
     1          even             -1
     2          odd              +1
     3          odd              -1
 
If the monomer functions are calculated from rotational constants (but not if
they are input explicitly from IASYMU), the symmetry types that are actually
included in the basis set may be restricted using the input variable ISYM. The
selection criteria that are possible in MOLSCAT version 11 and later are much
more general than in earlier versions.
 
In the current version, ISYM is interpreted bitwise; a particular asymmetric
rotor function is included if it passes ALL the appropriate tests.
 
   If bit 0 is set, odd  k functions are excluded
   If bit 1 is set, even k functions are excluded
   If bit 2 is set, functions with epsilon*(-1)**j = -1 are excluded
   If bit 3 is set, functions with epsilon*(-1)**j = +1 are excluded
   If bit 4 is set, functions with degeneracy 1 are excluded
   If bit 5 is set, functions with degeneracy 2 are excluded
   If bit 6 is set, functions with degeneracy 3 are excluded
   If bit 7 is set, functions with degeneracy >3 are excluded
 
To construct ISYM, start with 0 (including all functions) and add 2**n for each
class of functions to be excluded.
 
To decide which states are coupled, consider the symmetries (l,m) present in
the expansion of the intermolecular potential:
 
(1) If only terms with m even are present, functions with k even are not
    coupled to those with k odd.
(2) If only terms with (l+m) even are present, functions with epsilon*(-1)**j
    even are not coupled to those with epsilon*(-1)**j odd.
 
If either or both of these symmetries is present, it is most efficient to do
separate calculations for the (two or four) different sets.
 
For the special cases of J=0 and coupled states with K=0, there are additional
restrictions on the functions that are coupled: j+j'+l must be even, and
epsilon must be conserved. Do not be misled by these into believing that the
symmetries hold in more general cases.
 
For asymmetric rotors, all functions are in principle of degeneracy 1. However,
near-degeneracies can occur, and the program interprets these as degenerate if
the levels (from diagonalisation) are within a tolerance coded in subroutine
SET6C (usually 1.D-8). To be safe, do not set any high-bit flags for asymmetric
rotors.
 
The flags that test degeneracy are intended for use with spherical tops, and
allow A, E and F levels to be included selectively.
 
The levels to be included may also be restricted using the variable EMAX if
desired.
 
 
3.7 ITYP = 7
 
The basis set for ITYP = 7 is specified in the same way as that for ITYP = 2.
 
 
3.8 ITYP = 8
 
For atom - corrugated surface scattering, the JLEVEL array must contain a list
of (g1,g2) pairs specifying the surface reciprocal lattice vectors to be
included in the basis set. If NLEVEL = 0 on input, these will be calculated
from J1MAX, J2MAX and EMAX; g1 loops from -J1MAX to +J1MAX, and g2 loops from
-J2MAX to +J2MAX. However, not all these functions will be included in the
basis set, as described below.
 
The dimensions and symmetry of the surface unit cell are specified in the input
array ROTI. ROTI(1) and ROTI(2) are the lengths of the real space lattice
vectors in Angstroms (irrespective of the units of length used elsewhere).
ROTI(3) is the lattice angle in degrees.
 
To understand MOLSCAT's methods of generating basis sets for surface
scattering, it is important to realise that the operation is carried out in two
steps. At the time that the &BASIS NAMELIST block is read, MOLSCAT sets up a
master list of basis functions which MAY be included in subsequent scattering
calculations. This takes place before entering the loops over angles and
energies, so must be angle- and energy-independent. For each basis function G
= (g1,g2) covered by the loops over g1 and g2 described above, MOLSCAT checks
that the parallel kinetic energy (0.5*hbar**2/URED)*|G|**2 is less than the
input parameter EMAX, and includes the basis function in its master list only
if it passes this check. Note that the test involving EMAX is bypassed if
NLEVEL > 0 and the JLEVEL array is read in explicitly.
 
Subsequently, for particular values of THETA, PHI and ENERGY, MOLSCAT
calculates the parallel component of the incident momentum K, and selects from
the master list those basis functions for which (0.5*hbar**2/URED)*|K+G|**2 is
less than the input parameter EMAXK. This occurs even if the JLEVEL array is
specified explicitly in &BASIS data.
 
Thus, only those basis functions which satisfy both the EMAX and EMAXK criteria
will ultimately be included in the basis set. Since the EMAXK criterion is
usually the most sensible physically, EMAX serves principally to keep an
automatically generated master list within manageable bounds; the current
dimensioning of MOLSCAT does not allow the master list to contain more than 200
functions.
 
For the common case of surface scattering with the incident beam approaching
along a symmetry direction, MOLSCAT automatically constructs the appropriate
symmetrised linear combinations of basis functions. This takes place as part of
the second step described above, since it is not until that stage that the
program knows the incident angle.
 
For normal incidence scattering from square or hexagonal lattices, enormous
savings in computer time are possible if the full symmetry is accounted for.
Special versions of the routine SURBAS which take advantage of the symmetry are
available from JMH.
 
 
3.9  ITYPE=9: general user-supplied routine.
 
To facilitate writing user-supplied code which handles different collision
types than those described above, skeleton routines are provided, with
numerous comment cards, which provide a template for the required code.
 
 
3.10 Decoupling approximations
 
The following variables are specifically relevant to decoupling approximations.
 
JZCSMX   (default -1). By default, CS/DLD calculations are performed for all
         values of the body-fixed projection number m up to the largest diatom
         j value in the basis set. However, if cross sections are required only
         between the lowest few levels, this is unnecessary. If JZCSMX is set >
         -1 on input, m will be limited by JZCSMX instead of JMAX. Cross
         sections involving levels with j > JZCSMX are then not valid.
 
JZCSFL   (default 0). This is a historical remnant and values other than the
         default are not recommended. In CS calculations it sets the orbital
         quantum number in each channel as follows (with allowed values of
         JZCSFL = -1, 0, 1):
 
         L(I) = IABS( JTOT + JZCSFL*J(I) ).
 
IBOUND   (default 0). For spectroscopic applications using the helicity
         decoupling (coupled states) approximation, it is useful to be able to
         include the diagonal part of the Coriolis coupling exactly. This is
         achieved if IBOUND = 1 on input. Note, however, that the asymptotic
         matching still uses Bessel functions for integer l, so that the
         convergence with respect to RMAX may be slightly irregular when this
         option is used. This option is supported only for ITYPE = 21, 22, 23
         and 27.
 
         Another effect of IBOUND .EQ. 1 is to suppress coupled states
         calculations for projection quantum numbers greater than JTOT.
 
IOSNGP   an integer array of dimension 3. It specifies the number of (Gauss)
         integration points to use for orientation dependence of the scattering
         matrix. IOSNGP(1) is the number of points for theta. In ITYPE=105 and
         106, IOSNGP(2) is the number of points for phi; in ITYPE=103, the 3
         values are for theta(1), theta(2), delta phi.
 
         If values are not given (defaults are 0) the program will try to
         choose the minimum number needed for requested values of LMAX, MMAX
         (see &INPUT above) and/or input basis set rotor levels.
 
IPHIFL   (default 0) controls the type of numerical quadrature on phi for ITYPE
         = 103, 105 and 106. The default requests Gauss-Mehler (recommended)
         while IPHIFL.NE.0 requests Gauss-Legendre.
 
 
 
4. NAMELIST block &POTL
_______________________
 
Subroutine POTENL is used by MOLSCAT to evaluate the intermolecular potential
function at a given distance R as an expansion in appropriate angular
functions. The general-purpose version of POTENL supplied with MOLSCAT is
described in this section.  Simple potentials, whose coefficients can be
expressed as a sum of exponentials and inverse powers, can be input directly
as described in section 4.1.  For more complicated potential forms users
must supply their own potential routine(s).  This may be done by (1) using
the VSTAR mechanism described in section 4.2 to describe (some of) the
radial expansion coefficients, (2) using the VRTP mechanism described in
section 4.3 to provide an angle-dependent potential rather than radial
expansion coefficients, or (3) replacing the POTENL routine completely.  The
last method is often the most efficient as it may avoid repeating computations
required if the different potential terms are evaluated separately.  The
specification of the POTENL subroutine is described in detail in section 5.
Versions of POTENL that handle tabulated numerical potentials (which often
result from ab initio surfaces) by polynomial or spline interpolation are
available from SG.
 
The parameters that may be input in &POTL NAMELIST are as follows:
 
RM       is the length scaling factor that will be used by MOLSCAT. RM must be
         supplied in Angstroms (default 1.0), and defines the units of RMIN,
         RMAX etc. input in &INPUT. Subsequent calls to POTENL will also handle
         distances in these units.
 
EPSIL    is the energy scaling factor for the potential. EPSIL must be supplied
         in 1/cm, and subsequent calls to POTENL must return potential
         coefficients in these energy units. The value given to EPSIL does not
         affect MOLSCAT's interpretation of energies input in &INPUT and
         &BASIS.
 
MXLAM    is the number of terms in the potential expansion.
 
MXSYM    is a synonym for MXLAM.
 
LAMBDA   is an array specifying the symmetries of the MXLAM different terms. It
         is structured differently for the different values of ITYP; see the
         documentation for an initialisation call to POTENL in section 6.1 for
         more details. Note that potential symmetries specified in LAMBDA may
         be in any order and may be repeated, except for ITYP=7.
 
LVRTP    is a logical variable. If LVRTP = .FALSE. (the default), the potential
         is specified in terms of its expansion in angular functions. If LVRTP
         = .TRUE., subroutine VRTP is called as described in section 4.3 to
         evaluate the potential is specified at particular angles. The VRTP
         mechanism is also invoked if MXLAM.LE.0 on input, but this is only
         appropriate for IOS calculations.
 
NPT      is the number of Gauss-Legendre points (in theta) used in projecting
         out the angular components of the potential if LVRTP = .TRUE. but the
         calculations being performed are NOT IOS. NPT should be somewhat
         greater than the largest value of LAMBDA required in the potential
         expansion.
 
         Note that, if IHOMO .EQ. 2 (see below) then only the first (NPT+1)/2
         quadrature points are actually used.
 
NPS      is the number of secondary quadrature points (in r or phi) used in
         projecting out the components of the potential if LVRTP = .TRUE. but
         the calculations being performed are NOT IOS. For ITYPE = 5 or 6, NPS
         should be somewhat larger than the largest value of m in the potential
         expansion; for ITYPE=2, NPS should be somewhat larger than the largest
         value of v (but note that the version of the Gauss-Hermite routine
         supplied with the program at present supports only NPS = 2, 3, 4, 5
         and 10; this could be generalised simply by substituting another
         routine for supplying Gauss-Hermite points and weights).
 
         If ICNSYM .GT. 1 (see below), then NPS points are used on the range
         0 < phi < 2*pi/ICNSYM.
 
NTERM    is an array of MXLAM integers, describing how to evaluate the
         potential if LVRTP .EQ. .FALSE.. Each element of the NTERM array
         corresponds to one element in the expansion of the potential.
 
         If NTERM(I) is less than zero, this element of the potential array
         will be evaluated using the VSTAR mechanism described below.
 
         If NTERM(I) is positive, this element of the potential array will be
         evaluated as a sum of NTERM exponential or inverse power terms,
         specified by A, E and NPOWER.
 
 
4.1 Exponentials and powers; standard MOLSCAT POTENL routine
 
The following variables describe the input required when an element of the
potential array is to be represented as a sum of exponentials and inverse
powers.
 
NPOWER   For each positive value in the NTERM array, there must be NTERM values
         of NPOWER specified. If an element of NPOWER is 0, that potential term
         is an exponential described by A and E. If an element of NPOWER is
         negative, that potential term is an inverse power term described by A
         and NPOWER.
 
E        is an array of exponential factors. One value must be provided for
         each zero in the NPOWER array. N.b. values should be negative.
 
A        is an array of pre-exponential and pre-power factors. One value of A
         must be supplied for each number in the NPOWER array. If NPOWER(I) is
         0, the corresponding potential term is
 
         A(I) * EXP(E(IE)*R)
 
         while if NPOWER(I) is negative, it is
 
         A(I) * R**NPOWER(I)
 
CFLAG    For ITYPE=5 and 6, there are two common definitions of the potential
         expansion: the potential may be expanded either in terms of normalised
         spherical harmonics Ylm or in terms of renormalised spherical
         harmonics Clm. Internally, the program uses the former definition. If
         the coefficients are input in terms of renormalised functions, CFLAG
         should be set to 1 to instruct the program to multiply each input
         coefficient by an appropriate factor.
 
 
4.2 The VSTAR mechanism
 
If any element of the NTERM array is negative, subroutines VINIT, VSTAR, VSTAR1
and VSTAR2 must be supplied by the user. However, VSTAR1 and VSTAR2 will be
called only if the VIVS or WKB propagator is being used in a mode requiring
explicit derivatives (see section 2.12).  The dummy routines supplied with
MOLSCAT, if called, will print an error message and terminate the program.
 
VINIT will be called once for each negative value in the NTERM array during the
initialisation call to POTENL. The syntax of the call is
 
CALL VINIT( I, RM, EPSIL )
 
On entry, I is the index of the potential element in the NTERM (and LAMBDA)
arrays, and RM and EPSIL have the values read in in &POTL. None of these
arguments should be altered by the routine, but it may be desirable to store
their values in local variables so that they are available on subsequent calls.
VINIT should also read any data required for the potential evaluation.
 
VSTAR is called many times during evaluation calls to POTENL. The syntax of the
call is
 
CALL VSTAR( I, RR, SUM )
 
On entry, I is the index of the potential element required, and RR is the
intermolecular distance (in units of RM). VSTAR must evaluate the I'th
potential element and return its value in SUM (in units of EPSIL).
 
The specifications for VSTAR1 and VSTAR2 are identical to that for VSTAR,
except that they must return the first and second radial derivatives of the
I'th potential element respectively. For most propagators, the radial
derivatives are not used: in these cases, it is adequate to supply VSTAR1 and
VSTAR2 routines that simply print an error message and exit.
 
 
4.3 The VRTP mechanism
 
It is often more convenient to specify V(R,angles) explicitly than to expand
the potential in angular functions. The general-purpose version of POTENL
allows this for IOS calculations for ITYPE = 101, 102, 103, 105, and 106 and
for other calculations for ITYP = 1, 2, 5 and 6. The option is invoked by
specifying LVRTP = .TRUE. or (for IOS cases) MXSYM.LE.0); POTENL then expects
the potential to be supplied by a routine VRTP.  (N.b. specifying MXSYM.GT.0
and LVRTP=.TRUE. for an IOS case will cause Legendre terms to be projected
via the VRTP mechanism, but this is generally a very inefficient way to
hanlde IOS cases.)
 
The calling sequence is
 
CALL VRTP(IDERIV,R,V)
 
On an initialization call, IDERIV=-1, and RM(=R) and EPSIL(=V) can be set by
the routine or, if read in &POTL, used by the routine. The initialization call
should also set the variables IHOMO and ICNSYM in the common block ANGLES:
 
COMMON /ANGLES/ COSANG(3),FACTOR,IHOMO,ICNSYM
 
VRTP should set IHOMO=1 if the potential has heteronuclear symmetry or IHOMO=2
if it has homonuclear symmetry (with respect to theta), and ICNSYM to specify
the order of any rotational symmetry about the z axis. For ITYPE=103, ICNSYM is
used to specify heteronuclear or homonuclear symmetry for the second linear
molecule. Note that, for IOS calculations, IHOMO and ICNSYM would normally be
determined automatically by examining the LAMBDA array, but this can be done
only if the potential is expanded in angular functions.
 
Subsequent calls (IDERIV=0,1,2 for the potential and its first and second
derivatives respectively) require the routine to return in V the potential at
distance R and angles specified in the COSANG array. COSANG(1) is cos(theta)
and, for ITYP = 5 and 6, COSANG(2) is phi. For non-IOS ITYP = 2 cases,
COSANG(2) is q, the reduced harmonic oscillator coordinate, such that the
ground-state vibrational wavefunction of the diatom is exp(-q**2/2). For
non-IOS calculations, POTENL projects out the components of the potential using
Gaussian quadratures; note that the ITYP=2 code ASSUMES that the diatomic
molecule is a harmonic oscillator.
 
Some propagators do not use POTENL/VRTP calls with IDERIV .GT. 1, and for these
it is adequate to supply a VRTP routine that traps calls with IDERIV .GT. 0,
print an error message, and exits.
 
For ITYPE = 102, VRTP does not use COSANG(2), and must return a vector of
matrix elements <v1|V(R,theta)|v2> in the order expected by POTENL.
Appropriate communication is provided by a negative MXLAM in &POTL input,
with v1,v2 values supplied as LAMBDA(3*i-1),LAMBDA(3*i),i=1,abs(MXLAM);
n.b LAMBDA(3*i-2), which would normally have the order of the Legendre
polynomial, is not relevant and is ignored.
 
For ITYPE = 103, COSANG(1-3) are cos theta(1), cos theta(2) and phi(1)-phi(2).
The VRTP mechanism is not supported for non-IOS ITYP=3 cases in the present
version of MOLSCAT.
 
A sample VRTP routine is supplied with MOLSCAT.
 
 
 
5. User-supplied potential routines
___________________________________
 
As described above, many potentials can be specified either in terms of
exponentials and inverse powers or using a user-supplied VRTP or VSTAR routine.
It is best to use one of these mechanisms if it can be adapted to your needs.
However, in the rare cases where this is not possible, you will need to write a
complete POTENL routine. This section describes the specification that is
required of subroutine POTENL, in order to allow users to write their own
potential routines for complicated potentials.
 
In each run, POTENL is called once for initialisation purposes, and may on this
call read any data necessary to specify the potential. It returns information
about the terms present in the potential expansion for processing by MOLSCAT.
Subsequently, POTENL is called many times to evaluate the potential
coefficients for particular intermolecular distances.
 
The syntax of a call to POTENL is
 
CALL POTENL (IC,MXLAM,NPOTL,LAMBDA,RR,P,ITYP)
 
RR and P are REAL*8 arguments; the rest are INTEGER. LAMBDA and P are arrays
which should be dimensioned at LAMBDA(1), P(1) to switch off FORTRAN array
bound checking.
 
There are three basic types of call to POTENL;
 
IC = -1   Initialisation call. POTENL is called once with IC = -1, before any
          other calls to it, to allow it to read any necessary data and set up
          various parameters.
 
IC = 0    At subsequent calls to POTENL, IC is 0, and the routine must evaluate
          the intermolecular potential.
 
IC = 1,2  The VIVS propagator is most efficient if radial derivatives of the
          potential coefficients are available. If POTENL is called with IC = 1
          or 2, it must evaluate the IC'th radial derivative of each potential
          coefficient.
 
          The WKB integrator also requires first derivatives to start the
          integration (in locating turning points).
 
          For most other propagators, IC = 1 and 2 are not used, and it is
          adequate to supply a POTENL routine that prints an error message and
          exits if it is called with IC = 1 or 2.
 
 
 
The specification of POTENL for initialisation and evaluation calls will be
described separately.
 
 
5.1 Initialisation
 
IC       IC = -1 is the flag for an initialisation call.
 
MXLAM    On entry, MXLAM specifies the size of the LAMBDA array which has been
         provided externally. This value is used to check for array bound
         errors.
 
         On exit, MXLAM must specify the number of distinct terms in the
         expansion of the potential (ie. the size of the P array that will
         be returned by subsequent calls to POTENL.
 
NPOTL    On entry, NPOTL is not set.
 
         On exit, NPOTL must contain the appropriate value for the collision
         partners involved, specified by ITYP = MOD(ITYPE,10). The required
         values of NPOTL are
 
         ITYP = 1 to 6  NPOTL=MXLAM
 
         ITYP = 7 NPOTL=(KMAX+1), where KMAX is the order of the largest
                  Legendre component in the potential. See code in COUPLE for
                  precise use.
 
         ITYP = 8 This is complicated, and depends on the particular version of
                  SURBAS in use. Basically, NPOTL = 2 for the usual version of
                  SURBAS, and NPOTL = 6 or 8 for special normal incidence
                  versions (depending on symmetry of lattice). Existing
                  versions of SURBAS place the necessary value in COMMON/NPOT/,
                  and POTENL picks it up from there.
 
LAMBDA   Not set on entry.
 
         On exit, the LAMBDA array must contain indices specifying the symmetry
         of the potential terms that will be used. The LAMBDA array is used
         differently for each collision type (ITYP). Although it is externally
         a one-dimensional array, it is conceptually two-dimensional for some
         collision types, and may be handled explicitly as a two-dimensional
         array in POTENL if desired. Each element (or column) of LAMBDA
         corresponds to an element of the P array returned by subsequent calls
         to POTENL. MOLSCAT does not require that the symmetry terms be
         supplied in any particular order, but just that the Ith column of the
         LAMBDA array should correspond to the Ith element of the P array.
 
         Detailed specifications of LAMBDA for the different ITYP values
         follow. This should be read in conjunction with the documentation for
         the P array for an evaluation call.
 
         ITYP = 1:
 
         Potential is expanded in Legendre polynomials (these are
           unnormalized, such that P(2)=3*x*x-1).
         LAMBDA is a one-dimensional array.
         LAMBDA(I) contains the Legendre polynomial order of P(I)
 
         ITYP = 2:
 
         Potential is expanded in Legendre polynomials for each (v,v') pair.
 
         LAMBDA is a two-dimensional array LAMBDA(3, ).
         LAMBDA(1,I) contains the Legendre polynomial order.
         LAMBDA(2,I) contains the vibrational quantum number v.
         LAMBDA(3,I) contains the vibrational quantum number v'.
 
         Note that the matrix elements are invariant to exchange of v and v',
         and only one of these should be supplied.
 
         ITYP = 3:
 
         Potential is expanded as described by Green, JCP 62, 2271 (1975).
         LAMBDA is a two-dimensional array LAMBDA(3, )
         LAMBDA(1,I) is the index corresponding to l1
         LAMBDA(2,I) is the index corresponding to l2
         LAMBDA(3,I) is the index corresponding to the vector sum l = (l1+l2)
 
         Note that, for identical molecules, the potential is invariant to
         exchanging l1 and l2; however, for l1.ne.l2 BOTH terms MUST be
         supplied.
 
         ITYP = 5:
 
         Potential is expanded as a sum over angular functions
 
         [(Y(l,m) + (-)**m Y(l,-m))] / [(1 + delta(m,0))].
 
         The Y(l,m) are normalized spherical harmonics; note that V(0,0) then
         differs from the 'spherical average' by a factor. The angle theta is
         measured from the z-axis, which is the symmetry axis of the top. The
         angle phi is measured from the x-z plane, which must be a reflection
         plane in the current implementation.
 
         LAMBDA is a two-dimensional array LAMBDA(2, ).
         LAMBDA(1,I) is l(I).
         LAMBDA(2,I) is m(I).
 
         ITYP = 6:
 
         Specification of POTENL is the same as for ITYP = 5.
 
         ITYP = 7:
 
         LAMBDA(1,I) is the Legendre polynomial order;
         LAMBDA(2,I), LAMBDA(3,I), and LAMBDA(4,I), LAMBDA(5,I)
         are the diatom quantum numbers v,j and v',j' respectively.
 
         Note that the matrix elements are invariant to exchange of vj and
         v'j', and only one of these should be supplied.
 
         ITYP = 8:
 
         LAMBDA is a two-dimensional array LAMBDA(2, ).
         LAMBDA(1,I) and LAMBDA(2,I) are the reciprocal lattice indices
         corresponding to potential element P(I). They must be specified in the
         unique form returned by subroutine ORDER. This last requirement makes
         sure that the lattice symmetry is properly accounted for.
 
RR       Not set on input.
 
         On exit, RR must contain a length scaling factor which is applied to
         (virtually) all the distances used internally in MOLSCAT. It is
         specified in Angstroms. It is often convenient to set RR = 1.0D0 in
         the initialisation call to POTENL, and to handle everything in
         Angstroms thereafter.
 
P        Not set on input.
 
         On exit, P(1) must contain the energy scaling factor EPSIL to be used
         internally in MOLSCAT, and subsequent calls to POTENL must return
         energies in units of EPSIL. EPSIL is specified in 1/cm. It may
         be convenient to set EPSIL = 1.0D0 in the initialisation call to
         POTENL, and to handle everything in 1/cm thereafter. The value
         given to EPSIL here does NOT affect the interpretation of energy
         parameters input in &INPUT and &BASIS.
 
ITYP     On entry, ITYP is the collision type.
 
         If POTENL is coded specifically for a particular value of ITYP, it
         should check that the correct value is passed, as a precaution against
         the accidental use of the wrong executable version of MOLSCAT.  The
         value of this parameter should not be changed by POTENL.
 
 
5.2 Evaluation
 
For an evaluation call to POTENL, only the IC, MXLAM, NPOTL, RR and P arguments
are passed. LAMBDA and ITYP do NOT contain the values they were given in the
initialisation call, so these must be stored internally in POTENL if you need
them for an evaluation call.
 
IC       IC = 0, 1 or 2 is the flag for an evaluation call:
 
              IC = 0   evaluate the potential V
              IC = 1   evaluate dV/dR
              IC = 2   evaluate d2V/dR2
 
         Note that calls to POTENL with IC = 1 or 2 only occur for the VIVS
         propagator if IVP, IVPP, ISHIFT or IDIAG is set and for the WKB
         integrator. Even then, there is an option (controlled by the &INPUT
         logical variable NUMDER) which allows the derivatives to be evaluated
         numerically without making an IC = 1 or 2 call to POTENL. It is thus
         not altogether necessary for POTENL to cope with IC = 1 and 2 calls,
         but it should at least trap an attempt to call it this way and print
         an error message.
 
RR       The intermolecular distance at which the potential is to be evaluated,
         in units of RM (see the RR argument for an initialisation call to
         POTENL)
 
P        On exit, P(I),I=1,MXLAM must contain the potential array in the
         order specified earlier by the LAMBDA array returned by the
         initialisation call to POTENL.  The P array is required in units of
         EPSIL (see discussion of the initialisation call).
 
 
 
6. NAMELIST block &CONV
_______________________
 
If the variable ICONV in NAMELIST &INPUT is set to 1 on input, the program will
calculate S-matrices for successive values of the step size, RMIN, RMID or RMAX
and print out the root mean square (RMS) change in S-matrix elements and
transition probabilities each time. This provides an automated means of
choosing integration parameters capable of providing any required accuracy.
 
In this mode, the program performs NNRG calculations. Only a single energy
should be specified in the ENERGY array, and DNRG should be set to 0. Only a
single S-matrix is stored between calculations, so the program must not loop
over angular momenta or parity cases; thus JTOTU must be equal to JTOTL, and
MSET must be nonzero. Remember that, in some modes, MOLSCAT may determine RMIN,
RMID and RMAX internally, and it is safest to use the convergence testing with
these options switched off: IRMSET=0, RVFAC=0., IRXSET=0.
 
IVAR     (default 0) selects which variable is to be altered. Note that the
         first calculation is used as a "reference" calculation (unless ICONVU
         < 0, see below), so that the subsequent calculations must be less
         accurate than the first, not more accurate. For successive
         calculations, IVAR is used as follows: IVAR=0: step size is doubled
         each time. IVAR=1: RMIN is increased by DR each time. IVAR=2: RMID is
         increased by DR each time. IVAR=3: RMAX is decreased by DR each time.
 
DR       is the amount by which RMIN or RMID is increased or RMAX is decreased
         in successive calculations.
 
ICONVU   (default 0) is used if convergence information is to be transferred
         from one run of MOLSCAT to another. This is useful if the results
         obtained using two different propagators are to be compared. If ICONVU
         > 0 on input, the first S-matrix is written out (unformatted) to
         channel ICONVU; if ICONVU < 0, a previously saved S-matrix is read
         from channel |ICONVU|, and used as the reference S-matrix in
         calculating RMS errors.
 
 
 
7. Array dimensioning
_____________________
 
The main program for MOLSCAT declares one large array, X, which it passes to
the principal routine DRIVER. DRIVER and other routines then partition up the X
array according to the size of the scattering problem being tackled. Thus, very
few of the arrays used internally by MOLSCAT are explicitly dimensioned, and it
is seldom necessary for users to concern themselves with array dimensioning. If
MOLSCAT finds that the X array is not big enough, it will (in most cases) print
an error message and exit tidily; it is then necessary to re-run the program
with a larger X array declared in the main program. Note that the error message
specifies the storage required for the current allocation; additional storage
may be needed for subsequent allocations.
 
There are a few exceptions to this, concerning arrays which are either input as
data or are in COMMON, and thus cannot be flexibly dimensioned. Restrictions
arising from the dimensions of these arrays have been described in this manual.
 
 
 
8. COMMON blocks
________________
 
MOLSCAT uses a number of COMMON blocks internally, and the names of these
should be avoided when writing subroutines to link with the MOLSCAT code. The
named COMMON blocks used in MOLSCAT are:
 
DRIVE    MEMORY   CMBASE   PRBASE   INTPAC   ANGLES   VLSAVE   HIBRIN
LDVVCM   WKBCOM   EIGSUM   LATSYM   IOUTCM   ASSVAR   NPOT     POPT
 
 
 
9. Subroutines of the MOLSCAT system
____________________________________
 
Most subroutines in MOLSCAT are extensively commented; see the code for
details. The following descriptions list where the various subroutines are
called from, and in most cases give a brief description of their function.
 
AIRPRP   Subroutine called by AXSCAT
         Airy propagator routine
 
AIRYMP   Subroutine called by SPROPN
         Modulus and phase of Airy functions and derivatives
 
ASROT    Subroutine called by SET6C
         Calculates asymmetric rotor energies and wavefunctions
 
ASSLEG   Called by PASLEG
         calculates associated legendre polynomials
 
ASYME    Entry point in subroutine SET6, called by COUPLE
 
ASYMF    Entry point in subroutine SET6, called by COUPLE
 
ASYMG    Entry point in subroutine SET6, called by MCGCPL
 
AXSCAT   Subroutine called by STORAG
         Controlling routine for the log-derivative/Airy hybrid propagator
 
BASE     Subroutine called by DRIVER
         Handles generation of basis set
 
BASE9, BAS9IN, SET9, CPL9, DEGEN9
         Subroutine / entry points called from BASE etc.
         User-supplied routines to specify a special coupling scheme
 
BASIN    Entry point in subroutine BASE, called by DRIVER
         Initialisation entry for BASE - reads &BASIS data
 
CHCK6I   Subroutine called by SET6I
         Check asymmetric rotor functions for orthogonality
 
CHECK6   Subroutine called by SET6
         Check asymmetric rotor functions for orthogonality
 
CHKSTR   Subroutine called by DRIVER, etc.
         Checks that there is enough storage left in the X array
 
COLIM    Subroutine called by RMTPRP
 
CONVRG   Subroutine called by DRIVER
         Performs convergence checking if &INPUT ICONV=1
 
CORR     Subroutine called by AIRPRP
         Correction terms for Airy propagator
 
COUPLE   Subroutine called by BASE
         Handles angular momentum coupling elements
 
CPLOUT   Subroutine called by BASE
         Output routine for angular momentum coupling elements
 
CPL3     Subroutine called by COUPLE
         Coupling matrices for ITYPE = 3
 
CPL21    Subroutine called by MCGCPL
         Coupling matrices for ITYPE = 21
 
CPL23    Subroutine called by MCGCPL
         Coupling matrices for ITYPE = 23
 
CPL25    Entry in SET6 called by MCGCPL
         Coupling matrices for ITYPE = 25
 
CPL26    Subroutine called by MCGCPL
         Coupling matrices for ITYPE = 26
 
DAPROP   Subroutine called by AXSCAT (INTFLG = 8), DASCAT (INTFLG = 6)
         Propagation routine for the diabatic modified log-derivative method
 
DASCAT   Subroutine called by STORAG
         Controls the diabatic modified log-derivative propagator
 
DASIZE, DAOPEN, DACLOS, DAWR1, DAWR2, DARD1, DARD2
         Subroutines called by PRBR for in-core simulation of direct access
         files
 
DEGENF   Entry point in subroutine BASE, called by OUTPUT
         Returns degeneracy factor for denominator of cross-section expressions
 
DELRD    Subroutine called by VIVAS
         Calculates length of next step
 
DERMAT   Subroutine called by VIVAS WKB
         Calculates first or second radial derivative of potential matrix
 
DGEMUL   Subroutine called from AIRPRP QAPROP RMTPRP STABIL TRNSFM VIVAS
         Matrix multiplication (ESSL routine)
 
DGESV    Subroutine called from DVSCAT STABIL VIVAS YTOK
         Solves linear equations (LAPACK routine)
 
DMSYM    Subroutine called by ASROT
         Symmetrizes spherical top wavefunctions
 
DRIVER   Subroutine called by MOLSCAT main program
         Driver reads &INPUT data and handles the calls to the major routines.
 
DSYFIL   Subroutine called by AIRPRP LDVIVS RMTPRP TRNSFM WAVVEC YTOK
         Fills in upper or lower triangle of symmetric matrix
 
DVFREE   Subroutine called by DVSCAT
         Asymptotic matching for DeVogelaere algorithm
 
DVSCAT   Subroutine called by STORAG
         Main routine for DeVogelaere algorithm
 
DVSTRT   Subroutine called by DVSCAT
         Starts DeVogelaere propagation
 
EAVG     Subroutine called by DRIVER
         Provides energy values suitable for Boltzmann averaging
 
ECNV     Subroutine called by BASE DRIVER
         Handles different possible energy units and returns conversion factor.
 
ECNVX    Subroutine called by ECNV
         Handles character string data values in EUNITS
 
EPSUM    Subroutine called by OUTPUT
         Calculates S-matrix eigenphase sum from K-matrix
 
ESYMTP   Subroutine called by COUPLE SET6
 
F02AAF   Subroutine called by WAVEIG
         Eigenvalues of a real symmetric matrix
 
F02ABF   Subroutine called by ASROT DMSYM EPSUM POTENT QAPROP
         RMTPRP SHRINK VIVAS
         Eigenvalues and eigenvectors of a real symmetric matrix
 
FIND     Subroutine called by SURBAS
         Finds potential term coupling two G-vectors in surface scattering
 
FINDRM   Subroutine called by DRIVER
         For IRMSET > 0 option, finds suitable starting point for integration
 
FINDRX   Subroutine called by DRIVER
         Checks that RMAX is beyond centrifugal barrier and increments it if
         necessary
 
FSYMTP   Subroutine called by COUPLE SET6
 
GASLEG   Subroutine called by GAUSSP
         Returns points and weights for Gauss-Legendre quadrature.
 
GAUSHP   Subroutine called by POTENL (VRTP case)
         Returns points and weights for Gauss-Hermite quadrature.
 
GAUSSP   Subroutine called by IOSBGP
         Interface to GASLEG for Gauss-Legendre points and weights
 
GCLOCK   Subroutine called by DRIVER IOSDRV IOSCLC
         Timing routine
 
GDATE    Subroutine called by DRIVER
         Returns character string with current date
 
GET102   Subroutine called by IOSBIN
         Special ITYPE=102 input; dummy version supplied with MOLSCAT
 
GSYMTP   Subroutine called by MCGCPL SET6
 
GTIME    Subroutine called by DRIVER
         Returns character string with current time of day
 
HEADER   Subroutine called by DRIVER
         Writes or checks a header on the ISCRU scratch file to ensure that it
         is compatible with the current run.
 
HERM     Called by POTENL (VRTP case)
         Generates Hermite polynomials
 
IDPART   Subroutine called by BASE
         Handles identical particle symmetry for ITYP = 3
 
IOSBGP   Entry point in subroutine IOSBIN, called by IOSDRV
 
IOSBIN   Subroutine called by BASIN
         Processes &BASIS data for IOS cases
 
IOS1     Entry point in IOSBIN, called by IOSDRV
         Sets up points and weights for orientation quadrature
 
IOS2     Entry point in IOSBIN, called by IOSCLC
         Initializes values for the propagator in IOS cases
 
IOSCLC   Subroutine called by IOSDRV
         Main control of IOS: loops over energies and orientations and
         accumulates generalized IOS cross sections
 
IOSDRV   Subroutine called by DRIVER
         Sets up storage for IOS cases and then calls IOSCLC
 
IOSOUT   Subroutine called by IOSCLC
         Outputs IOS generalized and state-to-state cross
         sections
 
IOSPB    Subroutine called by IOSCLC
         Calculates pressure broadening cross sections for IOS cases
 
IPASYM   Subroutine called by SET6
         Checks symmetry of asymmetric rotor coefficients (ITYPE = 6)
 
ISUTP    Subroutine called by IOSCLC
 
IXQLF    Entry point in subroutine IOSBIN, called by IOSOUT IOSPB SIG6
 
J3J000   Subroutine called by COUPLE CPL21 SET6
         Recursive routine for Wigner 3-j symbols with zero projections
 
J6J      Subroutine called by COUPLE J9J SET6 SIXJ
         Recursive routine for Wigner 6-j symbol
 
J9J      Subroutine called by XNINEJ
         Recursive routine for Wigner 9-j symbol
 
KSYM     Subroutine called by YTOK
         Forces symmetry on K matrix
 
KTOS     Subroutine called by DASCAT DVSCAT LDVIVS QASCAT RMTPRP
         Converts the real symmetric K matrix into the S matrix
 
LDPROP   Subroutine called by LDVIVS
         Log-derivative propagator
 
LDVIVS   Subroutine called by STORAG
         Controls the hybrid log-derivative/VIVS propagator
 
MASK     Called by DRIVER
         Machine-dependent code to suppress floating-point underflows
 
MAXMGV   Subroutine called by POTENT
         Find largest element of vector
 
MAXMGV   Called by POTENT
         Maximum magnitude element of a vector
 
MCGCPL   Subroutine called by BASE
         Handles angular momentum coupling for McGuire-Kouri coupled states
         approximation
 
MHAACK   Subroutine called by DRIVER
         Prints a citation request for the HIBRIDON propagator
 
NEXTE    Subroutine called by DRIVER
         Estimates next energy set in resonance search option
 
ODPROP   Subroutine called by DASCAT
         Single-channel implementation of diabatic modified log-derivative
         propagator
 
ORDER    Subroutine called by FIND
         Takes account of lattice symmetry for Fourier components of
         atom-surface potential
 
OUTERR   Entry point in subroutine OUTPUT, called by DVSCAT
 
OUTINT   Entry point in subroutine OUTPUT, called by DRIVER
         Initialisation entry for OUTPUT
 
OUTMAT   Subroutine called by AIRPRP
         Read or write transformation matrix
 
OUTPCH   Entry point in subroutine OUTPUT, called by DRIVER
 
OUTPUT   Subroutine called by DRIVER
         Outputs S-matrices etc. and calculates state-to-state cross sections
 
PARITY   Function called by BASE COUPLE CSRTRT ESYMTP FCOEF
         FSYMTP GSYMTP MCGCPL PRBR ROTROT SET6 THREEJ
         Returns (-1)**argument
 
PASLEG   Called by POTENL
         Calculates normalized associated Legendre polynomials
 
PERT1    Subroutine called by VIVAS
         Calculates perturbation corrections for VIVAS propagator
 
PERT2    Subroutine called by VIVAS
         Calculates perturbation corrections for VIVAS propagator
 
PLEG     Called by POTENL (VRTP cases)
         Calcualtes Hermite polynomials
 
PLM      Subroutine called by IOSBIN
         Calculates associated Legendre polynomials
 
POTENL   Subroutine called by DRIVER WAVMAT DERMAT ODPROP
         Evaluates intermolecular potential at distance R
 
POTENT   Subroutine called by AIRPRP
         Calculates wavevector matrix and diagonalises average potential
 
PRBOUT   Entry point in subroutine PRBR, called by DRIVER
 
PRBR     Subroutine called by DRIVER
         Handles calculation of pressure broadening cross sections
 
PRBR3    Subroutine called by PRBR
         Pressure broadening code for ITYPE = 3
 
PRBR3R   Entry point in subroutine PRBR3, called by PRBR
 
PRBRIN   Entry point in subroutine PRBR, called by DRIVER
         Initialisation entry for PRBR
 
QAPROP   Subroutine called by QASCAT
         Propagation routine for the quasiadiabatic modified log-derivative
         method (INTFLG = 7)
 
QASCAT   Subroutine called by STORAG
         Controls the quasiadiabatic modified log-derivative propagator
 
RBES     Subroutine called by DASCAT DVFREE QASCAT RMTPRP
         Generates Riccati-Bessel functions
 
RDPCH    Subroutine called by OUTPUT
         Outputs cross sections
 
RMSBF    Subroutine called by YTOK
         Ratio of derivative to function value for modified spherical bessel
         functions of the third kind
 
RMSET    Subroutine called by FINDRM
         Chooses suitable RMIN (IRMSET > 0 option)
 
RMTPRP   Subroutine called by STORAG
         Main routine for R-matrix propagator algorithm
 
RSYM     Subroutine called by DVSCAT
         Forces symmetry on K-matrix in DeVogelaere algorithm
 
SCAIRY   Subroutine called by AIRYMP
         Scaled Airy function and derivatives
 
SET1     Entry point in subroutine SETBAS, called by BASE
         Handles basis set and energy levels for ITYP = 1
 
SET2     Entry point in subroutine SETBAS, called by BASE
         Handles basis set and energy levels for ITYP = 2, 7
 
SET3     Entry point in subroutine SETBAS, called by BASE
         Handles basis set and energy levels for ITYP = 3
 
SET5     Entry point in subroutine SETBAS, called by BASE
         Handles basis set and energy levels for ITYP = 5
 
SET6     Subroutine called by BASE
         Handles basis set and energy levels for ITYP = 6
 
SET6C    Subroutine called by SET6
         Generates asymmetric rotor basis sets from rotational constants
 
SET6I    Subroutine called by IOSBIN
         IOS version of SET6
 
SET8     Entry point in subroutine SURBAS, called by BASE
         Handles basis set and energy levels for ITYP = 8
 
SETBAS   Name of subroutine containing SET1 - SET5
 
SGNCHK   Subroutine called by RMTPRP
         Ensures consistency of eigenvector signs from one R step to the next
 
SHRINK   Subroutine called by RMTPRP
         Performs basis set contraction for R-matrix propagator algorithm
         (ISHRINK > 0 option)
 
SIG6     Subroutine called by IOSOUT
         Handles ITYP = 6 cross sections for IOS case
 
SIXJ     Function called by FCOEF FSYMTP PRBR PRBR3 ROTROT
         Calculates Wigner 6-j symbol
 
SPROPN   Subroutine called by AIRPRP
         Diagonal propagator for Airy method
 
STABIL   Subroutine called by DVSCAT
         Stabilisation routine for DeVogelaere algorithm
 
STEFF    Subroutine called by FINDRM
         Steffensen iteration for accelerated convergence on RMIN
 
STORAG   Subroutine called by DRIVER IOSCLC
         Sets up storage for and calls a propagator; all calls to propagators
         are currently done through STORAG
 
STRY     Subroutine called by RMTPRP
         Tests whether eigenvectors of potential are changing slowly enough to
         end R-matrix propagation
 
STSRCH   Called by ECNVX
 
SURBAS   Subroutine called by BASE
         Handles basis set for surface scattering (ITYPE = 8)
 
SWRITE   Subroutine called by OUTPUT
         Write unformatted S matrix
 
SYMINV   Subroutine called by DAPROP KTOS LDVIVS LDPROP QAPROP RMTPRP
         Calculates the inverse of a real symmetric matrix
 
THREEJ   Function called by COUPLE CSRTRT FCOEF FSYMTP MCGCPL ROTROT
         Calculates Wigner 3-j symbol with all projections zero
 
THRJ     Function called by CSRTRT ESYMTP FSYMTP GSYMTP MCGCPL PRBR PRBR3
         Calculates Wigner 3-j symbol with no restriction on projections
 
TRNSFM   Subroutine called by AIRPRP POTENT QAPROP RMTPRP SHRINK VIVAS
         Performs a similarity transform
 
TRNSP    Subroutine called by AIRPRP POTENT QAPROP RMTPRP SHRINK
         Transposes a matrix
 
VINIT    Subroutine called by the general-purpose version of POTENL.
         Initialises for calls to potential routines VSTAR, VSTAR1 and VSTAR2.
 
VIVAS    Subroutine called by LDVIVS
         VIVAS propagator
 
VRTP     Subroutine called by general-purpose version of POTENL
         User-supplied routine which may be called to evaluate an interaction
         potential which is not expanded in angular functions.
 
VSTAR, VSTAR1 and VSTAR2
         User-supplied routines which may be called by the general-purpose
         version of POTENL to evaluate the interaction potential and its first
         and second derivatives respectively.
 
WAVEIG   Subroutine called by AIRPRP
         Get eigenvalues of potential matrix
 
WAVMAT   Subroutine called by DAPROP DERMAT DVSCAT DVSTRT HEADER
         LDPROP POTENT QAPROP RMSET RMTPRP VIVAS WKB
         Calls POTENL to obtain potential coefficients, and forms potential
         matrix for scattering routines.
 
WAVVEC   Subroutine called by WAVMAT DERMAT
         Efficient routine to handle vector products required by WAVMAT
 
WKB      Subroutine called by STORAG
         WKB propagator for one channel problems
 
XNINEJ   Function called by CSRTRT ROTROT
         Calculates Wigner 9-j symbol
 
YRR      Function called by IOSBIN
         Bispherical harmonic for IOS rotor-rotor scattering
 
YTOK     Subroutine called by LDVIVS RMTPRP
         Calculates the K matrix from the log-derivative matrix
 
ZBES     Called by GASLEG
 
 
10. Machine-dependent features
______________________________
 
MOLSCAT is written in standard FORTRAN 77 as far as possible, but there are
inevitably a number of features which depend on the particular computer being
used. These will be described briefly here.
 
 
10.1 Main program
 
The MOLSCAT main program does not do any processing; it simply allocates
storage and calls DRIVER to do all the work.
 
If MOLSCAT terminates with the message
 
CHKSTR.  CANNOT PROVIDE REQUESTED STORAGE.
 
then it is usually sufficient to modify the main program to increase the
parameter MXDIM and recompile.
 
 
10.2 NAMELIST
 
Most of MOLSCAT's input is in NAMELIST format. This is not standard FORTRAN 77,
but is implemented in most compilers and is too attractive a feature to forego.
It does, however, introduce some quirks; for example, older CRAY versions of
NAMELIST could not cope with CHARACTER variables, so the variable LABEL is
handled in a peculiarly complicated manner.
 
For compilers that do not provide NAMELIST, it is usually possible to simulate
it using other compiler extensions. Code for doing this is provided in
commented-out form in the routines that read data, and the extra routines
needed are available from JMH.
 
 
10.3 Integer length
 
MOLSCAT obtains working storage by partitioning an array of 8-byte real
elements. On most machines, integers occupy only 4 bytes, so it is possible to
pack 2 integers into each 8-byte element. The variable NIPR, set in subroutine
DRIVER, must be equal to the number of integers that may be packed into 8
bytes. NIPR should be 2 on most machines, but 1 on a CRAY.
 
 
10.4 Date and time routines
 
MOLSCAT obtains the date and time of a run for output in the header by calls to
routines GDATE and GTIME. These are not standard, and must be simulated. GDATE
must return the current date as a CHARACTER*11, and GTIME must return the time
of date as a CHARACTER*9. In the last resort, they can be replaced by routines
that just return spaces.
 
 
10.5 CPU time routines
 
MOLSCAT outputs information on the CPU time taken by various steps, which it
obtains by calls to subroutine GCLOCK. This must also be simulated in a
machine-dependent manner; it is required to return the CPU time taken so far,
in seconds. As a last resort, it may return a result of zero.
 
 
10.6 Floating point underflow
 
Various routines used by MOLSCAT require that the result of an arithmetic
operation causing floating point underflow should be zero. MOLSCAT calls
subroutine MASK in order to set this, and MASK should call an appropriate
machine-dependent routine to suppress underflow. Some machines do this
automatically, or use compiler options to achieve the effect; for example, a
VAX ignores floating-point underflow if the compiler is invoked with the
qualifier /CHECK=NOFLOATUNDER.
 
Take care that the routine used does not use excessive CPU time.  For example,
the routine ERRSET can be very expensive indeed on some IBM machines, because a
complicated error-handling routine is called every time floating-point
underflow occurs; if available the IBM VS FORTRAN, CALL XUFLOW(0), is
generally preferable.
 
 
10.7 Linear algebra
 
MOLSCAT is usually distributed with FORTRAN versions of all the linear algebra
routines. However, on many machines it is preferable to use specially optimized
versions. Wherever possible, remove the FORTRAN versions and use calls to
locally available library routines.
 
This is particularly important on vector processors, where use of vectorised
versions of the BLAS routines is crucial. It is important that any user who
implements new options in MOLSCAT should perform matrix operations by calls to
the routines described below, both for ease of maintenance and to simplify the
creation of efficient versions for other computers.
 
The important routines called by MOLSCAT and their functions are:
 
DGEMUL      Matrix multiplication
DGESV       Solve linear equations
SYMINV      Invert symmetric matrix
F02AAF      Diagonalise symmetric matrix without eigenvectors
F02ABF      Diagonalise symmetric matrix with eigenvectors
 
MOLSCAT also calls BLAS (basic linear algebra subroutines) such as DAXPY, DDOT
etc (or single precision SAXPY, SDOT etc in the CRAY version) in many places.
 
Subroutine ODPROP (for efficient single-channel propagation) also requires
special treatment for vectorisation to be achieved, and there is a special
version of this routine for CRAYs and similar machines.
 
LAPACK and BLAS
 
In version 12, MOLSCAT was modified to use LAPACK linear algebra routines
wherever possible. LAPACK is the successor to LINPACK and EISPACK, and is
designed to provide near-optimum performance for large problems on as wide a
range of architectures as possible. Suppliers such as NAG and CRAY have already
included substantial parts of LAPACK in their standard libraries, and will be
including more in the future.
 
If possible, you should run MOLSCAT using LAPACK routines that are optimised
for your particular computer. However, if this is not possible, you can obtain
FORTRAN versions of the LAPACK routines from a NETLIB server: simply send an
email message containing a line such as
 
send dsyevx from lapack
 
to a NETLIB server such as netlib@ornl.gov (Oak Ridge National Lab) to obtain
the source for the LAPACK routine DSYEVX.
 
The LAPACK routines use BLAS (basic linear algebra subroutines) as much as
possible. BLAS level 1, level 2 and level 3 routines exist. You should use BLAS
routines optimised for your particular computer if possible. However, if no
optimised routines are available, you can get FORTRAN versions of the BLAS from
a NETLIB server by sending an email message containing a line such as
 
send dblas2 from core
 
to obtain the double-precision level 2 BLAS routines.
 
 
The linear algebra routines supplied with MOLSCAT
 
1) Matrix multiplication
 
MOLSCAT calls DGEMUL, which is a routine from the IBM ESSL library. In the
distributed version, DGEMUL calls the BLAS routine DGEMM. If the real ESSL
DGEMUL routine is available, use it; otherwise, use the best BLAS version of
DGEMM that you can find.
 
2) Symmetric matrix inversion
 
MOLSCAT calls SYMINV. Two versions of SYMINV are recommended. The first is a
pure FORTRAN routine, which on most machines is faster than LAPACK equivalents
for relatively small problems (N<70). The second calls the LAPACK routines
DSYTRF and DSYTRI to carry out the inversion. For optimum performance, you need
to test both routines on your machine.
 
Note that MOLSCAT really does require matrix inversion, despite the usual rule
to use linear equation solvers instead. This is because the propagators
involved save information from one step to the next, and this advantage is lost
if the problem is formulated in terms of linear equation solvers.
 
3) Linear equation solver
 
The speed of this routine is not critical for most propagators. MOLSCAT calls
the LAPACK routine DGESV directly.
 
4) Eigenvalues and eigenvectors of symmetric matrices
 
These routines are important for INTFLG = 3, 4, 7 and 8. MOLSCAT calls
diagonalisers by the NAG names F02AAF and F02ABF, and the NAG routines give
acceptable performance on most machines. However, the distributed version of
MOLSCAT provides routines that simulate F02AAF and F02ABF by calls to the
LAPACK routine DSYEVX.
 
10.8 File handling
 
MOLSCAT adheres to the FORTRAN 77 standard in its use of READ and WRITE
statements (including direct access files).
 
The OPEN statements use FILE='fname' parameters to associate FORTRAN unit
numbers with data set names.  These names override default names.  For
example, IBM OS/MVS and CMS use FTnnF001 as the file name for UNIT=nn.
For the former the //GO.FTnnF001 DD card must be replaced by a //GO.fname DD
card, where fname is one of the file names described below. For the latter
the equivalent FILEDEF FTnnF001 command must be replaced by FILEDEF fname
On UNIX systems the FILE='fname' parameter associates the I/O with a file
named 'fname' in the current working directory.
 
  The following files may be used by MOLSCAT, depending on the value of
parameters (identical to 'fname') in the &INPUT data set.
 
     fname   format       use
     ------  ---------  -------------------------------------
     ISCRU     no       Propagator scratch unit used if ISCRU.ne.0
     ISAVEU    no       S-matrix file written if ISAVEU > 0
     ISIGU     yes,DA   Updated cross section file if ISIGU > 0
     KSAVE     yes      Saved values for resonance search if KSAVE > 0
 
In the VAX implementation, it is also convenient to OPEN the main data file and
a supplied ISCRU file with the keywords SHARED and READONLY, so that several
jobs can access them simultaneously. The resulting OPEN statements are
nonstandard, and are commented out in the distribution version of MOLSCAT.
 
 
11. References
______________
 
It would be difficult to give a complete set of literature references for all
the various capabilities of MOLSCAT. The following is a selected list for
various aspects; it tends to reflect publications of the authors as the program
often follows these works rather closely.
 
ITYPE = 1
_________
A.M. Arthurs and A. Dalgarno, Proc. Roy. Soc. A256 540 (1963).
 
ITYPE = 2
_________
 
S. Green, J. Chem. Phys. 70, 4686 (1979).
 
ITYPE = 3
_________
 
S. Green, J. Chem. Phys. 66, 2271 (1975); J. Chem. Phys. 67, 715 (1977);
T.G. Heil et al., J. Chem. Phys. 68, 2562 (1978).
 
ITYPE = 5,6
___________
 
S. Green, J. Chem. Phys. 64, 3463 (1976); J. Chem. Phys. 70, 816 (1979).
 
Effective Potential approximation
_________________________________
 
H. Rabitz, J. Chem. Phys. 57, 1718 (1972).
 
Coupled states (centrifugal sudden) approximation
_________________________________________________
 
P. McGuire and D.J. Kouri, J. Chem. Phys. 60, 2488 (1974).
 
Decoupled L-Dominant (DLD) approximation
________________________________________
 
A. E. DePristo and M. H. Alexander, J. Chem. Phys. 64, 3009 (1976).
 
IOS approximation
_________________
 
R. Goldflam et al., J. Chem. Phys. 67, 4149 (1977).
 
Pressure broadening cross sections
__________________________________
 
S. Green et al., J. Chem. Phys. 66, 1409 (1977).
S. Green, J. Boissoles, and C. Boulet, JQSRT 39, 33 (1988).
 
R-matrix propagator
___________________
 
J.C. Light et al., J. Chem. Phys. 69, 3518 (1978).
 
Modified log-derivative propagator
__________________________________
 
D. E. Manolopoulos, J. Chem. Phys. 85, 6425 (1986).
 
Hybrid modified log-derivative/Airy propagator
______________________________________________
 
D. E. Manolopoulos and M. H. Alexander, J. Chem. Phys. 86, 2044 (1987).
 
WKB semi-classical 'propagator'
_______________________________
 
R. T Pack, J. Chem. Phys. 60, 633 (1974).